## Slide 1: Modeling Approaches and Transport Pathways
Vicky Freedman
Senior Technical Advisor
Los Alamos, NM, USA

## Slide 2: Outline
Conceptual model
Performance Assessment
Features, events and processes
Modeling complexity

## Slide 3: Conceptual Site Model (CSM)
“A conceptual site model is a written and/or illustrative representation of the conditions and the physical, chemical and biological processes that control the transport, migration and potential impacts of contamination (in soil, air, groundwater, surface water and/or sediments) to human and/or ecological receptors.”

## Slide 4: Repository CSM
Geochemistry of the waste form and radionuclide release rate
Geochemical interactions with container (metal drums and immobilized with cement or bitumen backfill)
Near-field aqueous and gaseous phase radionuclide transport (concrete or steel containers then stacked in the disposal tunnels w/ voids backfilled with cement mortar)
Far-field aqueous and gaseous phase radionuclide transport

## Slide 5: Radionuclide Transport
Radionuclides will be released from the repository into the geological environment and eventually transported to the biosphere
  Water flux through the wastes creates leachate
Rate of radionuclide transport is dependent on physical and chemical properties of wastes and near- and far-field environments
    Hydraulic conductivity
    Solubility of radionuclides
    Precipitation and dissolution
    Sorption properties
    Porosity and permeability
Hanford Integrated Disposal Facility

## Slide 6: Performance Assessment
Use of mathematical models to simulate the long-term behavior of engineered and geologic barriers in a nuclear waste repository
Methods of uncertainty analysis are used to assess effects of parametric and conceptual uncertainties
Can refer to the process, model, or collection of models used to estimate future doses to human receptors
Geologic Repository Diagram (Ruiz-Fresneda et al. 2023)

## Slide 7: Solute (Contaminant Transport)
Calculate the flow of water in the unsaturated zone, which is used to calculate contaminant transport
Vadose Zone
Calculate the flow of water in the saturated zone, which is used to calculate contaminant transport
Groundwater
Gaseous releases are transported using velocity estimates of stack release and meteorological data
Atmosphere
Waste form degradation provides source term for release to near-field environments (vadose zone and atmosphere)
Repository Release
Performance assessments generally executed with discrete models that are designed as modules with defined interfaces
Each model may be a separate code, where output from one code serves as input to another code

## Slide 8: Features, Events, & Processes (FEPs)

## Slide 9: FEPs
Feature: is a physical component of a system that influences a system performance
Event: a process that influences system evolution/repository performance over a time period that is short compared to the time frame being considered
Process: is a dynamic interaction between features, which operates over a long timeframe

## Slide 10: FEPs
Features
  Geologic setting
  Engineering controls
  Waste package dimensions and composition
  Waste form characteristics
  Contaminant characteristics
  Thermal loading
Events
  Earthquake
  Fire
  Human intrusion (e.g., drilling)
  Meteorite impact
  Accidents/unplanned events
Processes
  Infiltration/unsaturated flow/groundwater flow
  Waste form degradation
  Radioactive decay
  Hydrothermal activity

## Slide 11: Nuclear Energy Agency
International database (NEA 1999, 2006)
Additional project specific FEPs
  South Korea – KAERI (Hwang et al. 2006)
  USA – DOE Yucca Mountain (BSC 2005; SNL 2008; Freeze and Swift 2010)
  USA – DOE Nuclear Energy (Freeze et al. 2010; Freeze et al. 2011)
  USA – DOE Nuclear Energy (Jones 2011)
https://www.oecd-nea.org/upload/docs/application/pdf/2020-12/nea2549-features-events-processes-for-disposal.pdf

## Slide 12: FEP Analysis
Performed iteratively within the PA methodology
  FEPs are identified and screened
  FEPs are evaluated iteratively within the PA framework
  List must be comprehensive and complete so that measurable, observable, and significant effects on long-term repository system performance can be identified
Modeling is key component in the evaluation of FEPs
  Scenarios are constructed based on FEPs

## Slide 13: Scenario Development

## Slide 14: Translating CSM to Model Framework
What are the critical processes?
How much and what model complexity do the data support?
What is the best way to represent FEPs?

## Slide 15: Scenario Types
Normal Evolution
  Thermal, hydraulic, mechanical and biogeochemical evolution of the geosphere, as it currently exists
  Initial temperature of the disposal system will depend on the activity and radionuclide composition of radioactive waste and thermal properties of host rock
  At early times, temperature in the near-field will increase due to radioactivity, but decrease at later times due to decay of short-lived nuclides
Disturbance
  Seismic event
  Repository construction can be viewed as a disturbance, where after repository closure, it is a slow recovery to the initial state of the geological environment

## Slide 16: Normal Evolution
Unsaturated Zone Flow and Transport
Saturated Zone Flow and Transport
Infiltration
Effects of Decay Heat on Water Movement
In-Drift Physical and Chemical Environment
Water Diversion Performance of the Engineered Barriers
Waste Package and Drip Shield Degradation
Waste Form Degradation and Radionuclide Release
Engineered Barrier System Transport
Yucca Mountain Processes (DOE 2002)

## Slide 17: Disturbances
Volcanic eruption
Seismic activity
Human disturbance
Increased precipitation/infiltration
Floods
Fires

## Slide 18: CSM Translation
Computer models cannot precisely replicate all conditions of a disposal facility
  Computational constraints force simplifications
  Need to identify level of detail necessary to represent FEPs
  Compartmentalized models (e.g.; atmospheric, unsaturated zone, groundwater modeling)
Abstraction is used to simplify the information to be considered in a performance assessment
  Extent of simplification depends on modeling objectives (e.g. screening, predictive, etc.)
  Model to be sufficiently detailed to ensure that it yields valid results for the performance assessment

## Slide 19: Model Abstraction
Reduce the complexity of a model while maintaining the validity of the simulation outcome
  Impractical to solve complex models for different realizations to properly span range of uncertainty
Model-reduction techniques extract important features to identify underlying mathematical/physical structure
  Incorporate different physics-based assumptions to reduce computational complexity while maintaining the physics
Normalysa and GoldSim support streamlined model abstraction approaches
System Knowledge
Detailed numerical modeling
Reduced-Order Model (ROM)l

## Slide 20: Flow and Transport

## Slide 21: Contaminant (Solute) Transport Modeling
Saturated and unsaturated flow
  Calculates aqueous pressure and water fluxes
  May be influenced by heat and fluid density
Solute transport
  Requires information on flow
  Calculates concentrations
  May be influenced by chemical reactions and fluid density

## Slide 22: Hydrologic Flow Processes
Porous media
Fracture flow
  Can provide major conduits or barriers for fluid flows
Dual porosity
  Porous media system can be represented by two different interacting subsystems: the matrix and the fracture pore domain

## Slide 23: Hydraulic Conductivity (K)
Permeability (k) is a measure of the properties of the medium
Hydraulic conductivity (K) is a measure of flow through a porous media that considers the properties of the medium and the fluid
Obtained through aquifer testing (large-scale) and column testing (small-scale)
K= hydraulic conductivity (L/T)
k = intrinsic permeability (L2)
ρ = density of water (M/(L3)
g = acceleration of gravity (L2/T)
μ = dynamic viscosity (M/LT)
Units
L = length
M = mass
T = time

## Slide 24: Porosity
Porosity is a measurement of void space inside rock
Total porosity = total void space
Effective porosity = void space that contributes to fluid flow
Mobile vs. immobile porosity
Fine-grained sediments may have high total porosity, but lower effective porosity
Contaminant distributions within immobile porosity zones can be difficult to extract
Geophysical logging, laboratory analyses

## Slide 25: Porosity-Permeability Relationship
Both are properties of subsurface materials that are related to the number and size of the void space
  Porosity is a measure of a material’s ability to hold fluid
  Permeability is a measure of the ability of a material to transmit fluids
Sands and gravels are both porous and permeable (and make good aquifers)
Clays have high porosity but low permeability

## Slide 26: Advection-Dispersion Equation (ADE)
Advective Transport
Dispersive Transport
Sorption, Decay, etc.
Sink Source Mixing

## Slide 27: Solute Transport
Advection is the transport process where solutes flow with the bulk fluid phase (same velocity as the fluid phase)
Molecular diffusion is driven by concentration gradient
  Effective diffusion in porous media is based on diffusion coefficients in water (~10-9 m2/s) and a formation factor due to a resistance to flow relative to pure water
Steefel and Maher, 2009

## Slide 28: Dispersion
Dispersion describes the mixing of a solute due to fluctuations around the average velocity
  Defined as the product of the average fluid velocity and dispersivity
  Longitudinal dispersivity DL in the principle flow direction is typically higher than DT in the direction transverse to the main flow
  Dispersion in contaminant transport modelis is empirical and a strong function of scale, with larger dispersivity values observed at larger spatial scales
Freeze and Cherry 1979

## Slide 29: Sorption, Retardation, and Reactions
Ability of a chemical to sorb to soil particles is measured by its sorption partition coefficient, KD
Solid-phase concentration
Aqueous-phase concentration
Retardation uses Kd to account for the effects of sorption on solute transport
Distribution
Coefficient
Volumetric Water Content
Soil bulk density
λ is the constant of proportionality or decay constant; dependent on the radionuclide
Database link: Decay data search (lu.se)
Half-life
Decay constant

## Slide 30: Modeling Complexity

## Slide 31: What Is Complexity?
No universal definition of complexity - it is application specific
Universal axiom is to apply the principle of parsimony to all aspects of model development at the proper stage of development
Recommended modeling approach is to apply sufficient complexity so that the relevant features, events and processes (FEPs) are adequately represented to produce technically defensible results

## Slide 32: Level of Complexity
Dependent on
  Purpose of model
  Availability of hydrologic and geochemical data
  Justified level of geologic detail
  Scale of geologic features
Previous modeling experience
Start simple and build complexity carefully
WIPP conceptual model of geologic processes affecting transport (Kuhlman 2011)

## Slide 33: 3 Aspects of Complexity
Appropriate level of complexity needs to be identified with respect to the question that needs to be answered in the performance assessment process
Process of model development, and achieving the optimal balance in model simplicity and technical defensibility, is iterative
Freedman et al. 2017

## Slide 34: Modeling Approach
Numerical complexity
  Dimensionality
  Discretization
  Demand for high computational resources
  Range of spatial scales
Simulation complexity
  Uncertainty
  Calibration and validation
Full three-dimensional (3D) models can be large and difficult to use because of long run times and potential numerical stability issues
Simplified, reduced-order models (ROMs) may be needed
Glass cylinder arrays in lysimeters with the 2D representation of glass with equivalent surface area (Freedman et al. 2016)

## Slide 35: Physical and Geochemical Heterogeneities
Features impacting flow and transport
  Horizontal bedding
  Sloping interfaces
  Zones with contrasting permeabilities
Difficult to characterize from sparse data
Often represented by number of parameters used to characterize hydraulic conductivity distributions
  Stochastic methods
  Lithofacies
  Geostatistics
Biogeochemical heterogeneity is correlated to physical heterogeneities
  Stochastic methods
  Lithofacies
  Geochemical scaling functions

## Slide 36: Geologic Complexity Example

## Slide 37: Heterogeneity Comparison

## Slide 38: Breakthrough Curve at Water Table
Chart: Year

## Slide 39: Description of Process
Translating the conceptual model to a numerical modeling framework usually results in some simplifications of the actual FEPs, or their distribution at a site
Dependent on available data that define FEPs and the capabilities of the modeling tool(s) selected
The appropriate level of description can be evaluated by incrementally adding process complexity to a simple model, or by removing it from a highly complex model
Truex et al. 2012

## Slide 40: Geochemical Processes
Common approach is to lump chemical processes such as sorption, co-precipitation and ion exchange into a single retardation term (no kinetics)
  Sorption is defined as the removal of solutes from solution onto mineral surfaces
  Described as a distribution coefficients (Kd)
Cementitious waste form modeling generally uses Kd approach
Glass waste form modeling generally uses a reactive geochemical approach describing hydrolysis, glass dissolution, secondary precipitates, and subsequent porosity and permeability changes
Compositions of cementitious waste forms and LAW Reference Glass (Freedman et al. 2014; 2016)

## Slide 41: Constraints
Computational resources
Time to achieve modeling objectives
Code availability
Serial computation
Numerical stability

## Slide 42: Numerical Constraints
Courant Number
Peclet Number (ratio of advection to diffusion/dispersion)
  Large number indicates advectively dominated flow
  Small number indicates diffusively dominated flow
  =
Near-field glass emplacement
in Hanford IDF

## Slide 43: Some (not all) Issues of Scale
Parameters
  In situ parameters differ from those measured in the laboratory on cores
  Laboratory spatial scale is much smaller than the dimensions of model cells
Grid discretization
  Spatial resolution for transport simulations is usually finer than for groundwater flow
  Rule of thumb aspect ratio of maximum of 20:1
  Courant number relates timestep size and solute velocity to grid-block size (v(∆t)/∆x)
Transport
  Dispersion is a scale-dependent parameter describing spreading

## Slide 44: Incorporating Complexity
Develop conceptual site model using FEPs
  Description of Heterogeneity
    Geology (extent of physical and chemical heterogeneity)
  Description of Process
    Waste form degradation (reactive vs. non-reactive)
    Solute/radionuclide transport
    Fracture flow
    Heat transport
Modeling Approach
  Dimensionality
  Code selection
  Gridding/Parameterization

## Slide 45: Exposure, Dose and Risk Assessment

## Slide 46: Characterizing Risk
Risk
Assessment
Dose Assessment
Exposure Assessment
Environmental Modeling
4
Risk Assessment
Combines information obtained from dose-response relationship and exposure assessment to describe the carcinogenic risk associated with expected human exposures
3
Dose Assessment
You can simply impress your audience and add a unique zing.
2
Exposure Assessment
Process of identifying group(s) of individuals at risk using the various routes (pathways) of exposure and their magnitude, frequency, and duration
1
Environmental Modeling
Concentration estimates in air, water, soil, etc. are identified at compliance points and used to support exposure assessments

## Slide 47: Modular Approach
For near-surface disposal facilities, the potential release of gaseous contaminants needs to be identified.
Atmospheric Fate and Transport
Any contaminants reaching the water table are simulated in a groundwater flow and transport model
Groundwater Fate and Transport
Identify the loading and waste form release rates
Waste Form Release
For near-surface disposal facilities, the release of key contaminants into the vadose zone is simulated
Vadose Zone Fate and Transport
The concentrations from each model are used to determine lifetime cancer risk from all radionuclides in all exposure pathways
Radiological Risk Assessment

## Slide 49: Characterizing Risk
Risk
Assessment
Dose Assessment
Exposure Assessment
Environmental Modeling
4
Risk Assessment
Combines information obtained from dose-response relationship and exposure assessment to describe the carcinogenic risk associated with expected human exposures
3
Dose Assessment
You can simply impress your audience and add a unique zing.
2
Exposure Assessment
Process of identifying group(s) of individuals at risk using the various routes (pathways) of exposure and their magnitude, frequency, and duration
1
Environmental Modeling
Concentration estimates in air, water, soil, etc. are identified at compliance points and used to support exposure assessments

## Slide 50: Exposure Pathway: Soil
Consumption
Vegetables, fruits, and grains grown in the contaminated soil
Milk and meat obtained from livestock that eat pasture grass grown in the contaminated soil
Direct Consumption
Ingestion of contaminated soil
Inhalation
Inhalation of radionuclides from contaminated surface soil suspended in the air
External Exposure
External exposure to contaminated soil

## Slide 51: Exposure Pathway: Groundwater
Consumption
Use of water for agricultural purposes, such as watering of livestock; irrigation of vegetables, fruits, and grains; and irrigation of pasture grass consumed by livestock
Direct Consumption
Direct ingestion of water from the contaminated source

## Slide 52: Exposure Pathway: Surface Water
Consumption
Use of water for agricultural purposes, such as watering of livestock; irrigation of vegetables, fruits, and grains; and irrigation of pasture grass consumed by livestock
Direct Consumption
Direct ingestion of water from the contaminated source
Consumption of aquatic foodstuffs (such as fish) obtained from the contaminated source
External Exposure
External exposure to the contaminated source during such activities as swimming, boating, and residence along contaminated shorelines

## Slide 53: Exposure Pathway: Air
Consumption
ingestion of radionuclides incorporated into foodstuffs (vegetables, fruits, grains, meat, and milk) due to deposition of airborne particles
Direct Consumption
Ingestion of contaminated soil and foodstuffs due to deposition of airborne particles
Inhalation
Inhalation of airborne radionuclides in the source compartment
Inhalation and external exposure to airborne radionuclides in the source compartment
External Exposure
External exposure to airborne radionuclides in the source compartment
Exposure to radionuclides deposited on vegetation and the ground surface

## Slide 54: Exposure Scenarios
Identifies estimates of exposure, dose, and risk and includes facts, data, assumptions, inferences, and professional judgment about how the exposure takes place; e.g.
  Resident Farmer
  Residential Tap Water
  Inadvertent Human Intruder
  Subsistence Fishing Native
  Construction Worker
  Indoor Worker
Exposure Pathways in the Risk Assessment Information System Resident Tap Water Scenario
(https://rais.ornl.gov/tools/rais_rad_risk_guide.html)

## Slide 55: Radiation Human Health Assessment Approaches
Risk
Risk is calculated directly by assigning a unit of risk for every unit of exposure (Cancer Slope Factor) and multiplying by the total exposure.
Risk = Exposure X Cancer Slope Factor
(slope factors exist for each radionuclide and route of exposure
DOSE
Dose is calculated by multiplying a dose conversion factor by the total intake/exposure. The calculated dose can also be multiplied by a probability coefficient to arrive at a risk value.
Dose = Exposure X Dose Conversion Factor
(each radionuclide has unique DCF)

## Slide 56: Radiation Assessment Approaches
Dose and Risk are closely related
Most national and international guidelines and standards for radiation protection are in terms of dose or concentration
Dose values may be converted into risk and vice versa using conversion factors
Risk = (total dose) X (probability coefficient in risk/unit dose)
Converted values may be somewhat different than directly-calculated values
  Risks converted from dose may vary as much as 10 times from risks based on slope factors for some types of exposure

## Slide 57: Summary
Build a model for a specific purpose and carefully examine the need for complexity
  Modeling is iterative
  Models are updated based on new
    Data
    Evolving goals and questions
    New conceptualizations and FEPs
Guiding principles in building models
  Start simple, then add complexity as needed
  Identify behavior with sufficient level of complexity, and simplify
  Performance assessments are modular and need to think about how outputs from one model impact subsequent modeling steps
Environmental modeling supports risk assessment

## Slide 58
All involved parties (researchers, consultants, site managers, regulators and the public) may understand modeling differently and the benefits of considering complexity with FEPs

## Slide 59: References
BSC (Bechtel SAIC Company) 2005. The Development of the Total System Performance Assessment-License Application Features, Events, and Processes. TDR-WIS-MD-000003 REV 02. Las Vegas, Nevada: Bechtel SAIC Company
Hwang, Y.S; Kang, C.H.; and Soo, E.J. 2006. Development of the KAERI FEP, Scenario, and Assessment Method Database for Permanent Disposal of HLW in Korea. Progress in Nuclear Energy Volume 48, Issue 2 pp 165-172. Daejeon, South Korea: Korea Atomic Energy Research Institute.
Jones, R.H. 2011, Features, Events, and Processes for the Disposal of Low Level Radioactive Waste - FY 2011 Status Report, Revision 0, Prepared for U.S. Department of Energy Used Fuel Disposition Campaign, FCRD-USED-2011-000297
Freeze, G.; and Swift, P. 2010. Comprehensive Consideration of Features, Events, and Processes (FEPs) for Repository Performance Assessments. PSAM 10 Conference Proceedings. Seattle, Washington: International Association for Probabilistic Safety Assessment and Management.
Freeze, G., Mariner, P., Blink, J.A., Caporuscio, F.A., Houseworth, J.E., and Cunnane, J.C. 2011. Disposal System Features, Events, and Processes (FEPs): FY11 Progress Report. SAND2011-6059P, Sandia National Laboratories, Albuquerque, New Mexico.
Kuhlman, K.L. 2011. Hydrogeology and WIPP Compliance – 11658. Waste Management Symposia, February 27 – March 3, 2011, Phoenix, Arizona.
Ryan, J. and V. Freedman. 2016. A Strategy for Maintenance of the Long-Term Performance Assessment of Immobilized Low-Activity Waste Glass, PNNL-23503, Rev. 1, Pacific Northwest National Laboratory, Richland, Washington.
Ruiz-Fresneda, M.A. M.F. Martinez-Moreno, C. Povedano-Priego, M. Morales-Hidalgo, M.L. Merroun. 2023. Impact of microbial processes on the safety of deep geological respositories for radioactive waste. Frontiers in Microbiology, Vol.14, https://doi.org/10.3389/fmicb.2023.1134078.
SNL (Sandia National Laboratories) 2008. Features, Events, and Processes for the Total System Performance Assessment: Analysis. ANL-WIS-MD-000027 REV 01. Las Vegas, Nevada: Sandia National Laboratories, Albuquerque, New Mexico.
Vienna, J.D., et al., Current Understanding and Remaining Challenges in Modeling Long-Term Degradation of Borosilicate Nuclear Waste Glasses. International Journal of Applied Glass Science, 2013. 4(4): p. 283-294.

## Slide 60
Gunalchéesh, Háw'aa, T’oya̱xsut ‘nüüsm