## Slide 1
High Frequency (HF) vertical ionospheric soundings
Michael Pezzopane (Piece of bread)
michael.pezzopane@ingv.it
Istituto Nazionale di Geofisica e Vulcanologia, 00143, Rome, Italy

## Slide 2
Region of the atmosphere where the ion and electron density reaches values as to influence the refraction index of radio waves (3kHz – 30MHz).
The ionospheric plasma is mainly due to the photoionization of atmospheric gases caused by the UV and X electromagnetic radiation coming from the Sun.
It is a very low-density plasma immersed in the geomagnetic field (magnetoplasma).
500 km
50 km
Stratopause
Thermopause
The terrestrial ionosphere

## Slide 3
The ionosphere acts as a big electromagnetic mirror that refracts and reflects signals transmitted from the Earth towards the ground.
This makes it possible radio connections between sites on the terrestrial surface that cannot see each other because of both the Earth’s curvature and obstacles, like for instance mountains.
It affects the electromagnetic wave propagation and then its study is important for Earth-Earth, satellite-Earth, and satellite-satellite communication purposes.
The terrestrial ionosphere

## Slide 4
D region: between 60÷90 km of altitudes and mainly responsible for the radiowaves absorption.
E region: between 90÷150 km of altitudes and reflects medium and long radiowaves (λ > 100 m).
F region: between 150÷400 km of altitudes and reflects the short radiowaves (λ < 100 m).
The terrestrial ionosphere
km
Notes: 4

## Slide 5
Tx
Rx
Possible Ionospheric Propagations: Oblique and Vertical
Oblique propagation
Vertical propagation
We will focus
on this method
Increasing the transmitted frequency, in the oblique case we go farther, in the vertical case we go higher. Anyhow, there will be a value of the frequency beyond which the signal penetrates the ionosphere without being reflected.

## Slide 6
Importance of the chosen frequency for oblique propagation: the case of the « Dirigibile Italia » airship
Survivors, by using a portable high frequency (HF) radio transmitter, tried unsuccessfully to send SOS messages and to establish a radio link with the ship “Città di Milano” of the Italian Navy, closely anchored at King's Bay. Only after 9 days of repeated radio‐distress transmissions, a Russian radio amateur close to the town of Arkhangelsk about 1,900 km away was able to receive the messages launched by the survivors and raise the alarm.

## Slide 7
N is the electron density per unit volume, m the electron mass, e the electron charge and ε0 the electric permittivity of the free space.
fN is called plasma frequency and represents the frequency with which the electrons oscillate around the ions if displaced from their equilibrium position, for instance because of the the perturbing electric field E of the electromagnetic wave propagating through the ionospheric plasma.
A plasma can be considered neutral over temporal scales greater than the corresponding oscillation period τ>>1/ωN.
The Plasma Frequency

## Slide 8
The gyrofrequency is the angular frequency of the circular motion of a charged particle in the plane perpendicular to the magnetic field defined by the following relation:
H is the magnetic field, μ0 the magnetic permeability of the free space, q the charge of the particle, and m the mass of the charged particle.
The Gyrofrequency

## Slide 9
The magnetoionic theory is concerned with the propagation of electromagnetic waves through a magnetoplasma.
Specifically, the reflection of the wave occurs when the ionospheric refractive index is equal to 0  n = 0.
Altar-Appleton
equation
The magnetoionic theory -> the Altar-Appleton equation

## Slide 10
After transmitting through a magnetoionic medium an electromagnetic wave with a certain polarisation, two waves propagate through it; these two waves have the same frequency, different phase velocity and different polarisation. This phenomenon is called magnetoionic birefraction of the electromagnetic wave into the magnetoplasma.
Simply speaking, a wave with a generic polarisation can be thought as the resultant of two waves;
if the wave propagates through an isotropic medium the two components are indiscernible;
if the wave propagates through an anisotropic medium (as it is the case of a magnetoionic medium) the two components are instead observable.
The Altar-Appleton equation neglecting collisions reflection conditions
→

## Slide 11
km
MHz
f>fNmax
f≤fNmax
Vertical Ionospheric Soundings - Ionograms

## Slide 12
How the Ionogram trace varies along the day
km

## Slide 13
Radiowaves of variable frequency are transmitted vertically towards the atmosphere. The ordinary mode of the transmitted wave is reflected from the ionosphere when the transmitted frequency matches the electron plasma frequency:
Depending on the reflection height there will be a definite time delay according to the relation:
The experimental trace is then a plot of the virtual height of reflection vs the transmitted frequency, which is called ionogram.
ordinary
extraordinary
km
Correspondence vertical electron density profile – ionogram trace

## Slide 14
E layer
F1 layer
F2 layer
Night
Day
km
Ne (cm-3)
km
100
200
300
400
500
102
103
104
105
NmF2
NmF1
NmE
Correspondence vertical electron density profile – ionogram trace

## Slide 15
Nighttime ionogram
Daytime ionogram
Daytime and Nighttime ionograms

## Slide 16
From the analysis of an ionogram several important characteristics (like the critical frequencies and the heights of the different ionospheric layers) can be found, that have a significant role in the studies concerning ionospheric physics, space weather and related phenomena.
foE
foF1
foF2
NmE
NmF1
NmF2
Why electron density maxima of the profile correspond to ionogram cusps?

## Slide 17
km
Why electron density maxima of the profile correspond to ionogram cusps?
foE
foF1
foF2
NmE
NmF1
NmF2

## Slide 18
Influence of the geomagnetic field on the ionogram trace

## Slide 19
Influence of the geomagnetic field on the ionogram trace

## Slide 20
From the analysis of one ionogram several important characteristics (like the critical frequencies and the heights of the different ionospheric layers) can be found, that have a significant role in the studies concerning ionospheric physics, space weather and related phenomena.
foE
foF1
foF2
h’E
h’F1
h’F2
Importance of ionogram interpretation

## Slide 21
The necessary work to obtain the ionospheric characteristics from an ionogram is called “ionogram interpretation or ionogram scaling”.
Till a few decades ago this interpretation was performed only manually by expert operators with a ruler and a pencil.
Now, luckily, there are softwares that help the operators to accomplish this demanding (but valuable) work.
During the hands-on session you will try to become an IONOGRAM SCALER!!!!
The ionogram scaling

## Slide 22
In the last decades, the importance of having real time ionospheric data for space weather purposes has greatly increased. For this reason since 80s much work has been performed to develop computer programs able to automatically scale the ionograms giving as output the standard ionospheric characteristics along with an estimate of the electron density profile.
Though much progress has been made, still today a significant effort is invested in upgrading these programs in order to improve their reliability.
Autoscaling of an ionogram

## Slide 23
Autoscaling of an ionogram

## Slide 24
Autoscaling of an ionogram

## Slide 25
Autoscaling of an ionogram

## Slide 26
Autoscaling of an ionogram

## Slide 27
Autoscaling of an ionogram

## Slide 28
Autoscaling of an ionogram

## Slide 29
Autoscaling of an ionogram

## Slide 30
Sporadic E layer
Different types of ionograms

## Slide 31
Different types of ionograms
flat reflector
Spread F
Notes: Presence of plasma irregularities that causes the reflection of the same frequency at different heights and so with different delay times. Consequently, the trace is not defined, spread.

## Slide 32
Different types of ionograms
Multiple reflections

## Slide 33
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics at different latitudes.
Importance of ionosonde stations
positive phase
negative phase
Rome – March 2015 event
INGV Ionospheric portalhttp://eswua.ingv.it/

## Slide 34
Importance of ionosonde stations
Rome and Malindi – September 2023 event
INGV Ionospheric portalhttp://eswua.ingv.it/
positive phase
negative phase
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics at different latitudes.

## Slide 35
Importance of ionosonde stations
Two solar flares occurred on 6 September 2017 at 08:57 UT (X2.2) and at 11:53 UT (X9.3)
normal propagation
absorption
ionosphere
Notes: The study and the real-time monitoring of the ionosphere are important for Space Weather purposes. During a solar flare, if this is enough energetic and occurs on the Sun side towards the Earth, some of the released X rays penetrate the terrestrial atmosphere till the lower altitudes of the ionosphere, causing an increase of ionization and then an increase of the absorption suffered by the electromagnetic wave.

## Slide 36
Absorption of the signal transmitted by the ionosonde from about 9 UT to 13:30 UT!!!
Rome - September 2017 event
Importance of ionosonde stations
INGV Ionospheric portalhttp://eswua.ingv.it/

## Slide 37
Importance of ionosonde stations
km
foE
foF1
foF2
NmE
NmF1
NmF2

## Slide 38
AIS-INGV - August 2007
Conclusion
Tucuman

## Slide 39
AIS-INGV + Autoscala
Conclusion
Now the Australian Space Weather Forecasting Centrehttps://www.sws.bom.gov.au/

## Slide 40
It only runs under the Windows system
Hands-0n session –> Scaling of foF2 from Malindi ionograms

## Slide 41
Hands-0n session –> Scaling of foF2 from Malindi ionograms
Ionospheric characteristic  foF2
Ionospheric station  Malindi
Ionograms from August 2023: days 06, 07, 08, 09, 12 and 13
Time resolution: 15 minutes (maximum 96 ionograms per day)
Step 1: scaling of foF2 for all the ionograms of the day
Step 2: plot of the foF2 values (Excel? Python? Matlab? Choose the way you prefer)
Step 3: COMPARISON BETWEEN YOUR RESULTS AND MINE!!!
Team 1  06 August 2023
Team 2  07 August 2023
Team 3  08 August 2023
Team 4  09 August 2023
Team 5  12 August 2023
Team 6  13 August 2023

## Slide 42
Thank you!!

## Slide 43
Backup slides

## Slide 44
Why is the ionosphere characterized by electron density maxima?
The existence of the ionospheric layers is due to the fact that the density of atoms that can be photoionized decreases with the height while the intensity of the radiation increases; these two opposite effects produce a maximum in the vertical electron density profile. To this maximum one makes it correspond an ionospheric layer.
The Ionosphere: some physical characteristics

## Slide 45
Why is the ionosphere characterized by different layers?
Since the different molecolar species present in the atmosphere are vertically stratified, and react differently to the solar radiation, the vertical electron density profile is characterized by several relative maxima and minima that identify different ionospheric layers; one makes the main layers correspond to the ionospheric regions.
The Ionosphere: some physical characteristics

## Slide 46
Frequenze criticheCuspidi dello ionogramma
since μ’=1 at the base h0 of the ionosphere
In the absence of magnetic field and collisions, the refraction index is μ2=1-(f2N/f2) and μμ’=1; then also μ’ is function of fN.
Vertical Ionospheric Soundings: ionogram cusps

## Slide 47
The most accredited theory today for the explanation of the formation of sporadic E layers is the windshear theory, i.e. it is believed that these layers are created by the drift vxB, where v refers to the speed of the zonal neutral wind. Ion dynamics at typical E-region heights are dominated by collisions. When there are zonal neutral winds towards W and towards E (or better still towards W but slower), the presence of a B causes an accumulation of ions to be created in the central zone which gives rise to an E and therefore an accumulation of electrons.
Sporadic E layer

## Slide 48
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics.
Importance of ionosonde stations