## Slide 1
ESA Space Weather services
Alessandra Di Cecco, PhD
Italian Space Agency

## Slide 2: ESA Space Safety Programme (S2P)
Objectives:
  Protect space assets
  Protect daily services
  Protect public and private investments
  Protect astronauts in space
  Protect life on our planet
ESA S2P address three main topics:
  Space Debris
  Near-Earth Objects (NEO)
  Space Weather
Credit: ESA

## Slide 3: ESA Space Safety Programme
Space Debris orbits
Space Debris orbits
Space Weather

## Slide 4: Sun’s internal structure
Hydrostatic Equilibrium between Radiation Pressure and Gravity
Nuclear fusion of H in He (differently by nuclear reactors)
Energy transport:
  Radiative zone
  Convective zone
Photon scattering path from core to surface: 100.000-1.000.000 yr
Neutrinos travel straight: no matter interaction
Credit: NASA / H. Smithsonian

## Slide 5: Sun’s surface phenomena
Core Temperature | 15 106 K
Photosphere Temperature | 6 103 K
Corona Temperature | 1-3 million K
Credit: NASA/Goddard
Solar atmosphere:
  Chromosphere
  Corona
Solar wind

## Slide 6: Sunspots
Sunspots approx. 4000 K
11-years cycle
Magnetic activities
and field lines
Credit: NASA

## Slide 7: Solar eruptions and coronal holes
Flares: Brightness flash near Sunspot
CME: Coronal Mass Ejection Shock waves
Magnetic field lines reconnection
Strong X-ray emission
Solar wind emission (H, alpha, e- ) High kinetic energy particles (10KeV) supersonic wind plasma emission magnetosonic waves
Credit: NASA Solar Dynamic Observatory (SDO)

## Slide 8: Space Weather (SWE)
Solar Activity affects the space environment:
Satellite interference in radio signal or sub-system damage
Geomagnetic storms and substorms
Aircraft passenger exposed to radiation
Problem to transmission lines
Magnetosphere effects

## Slide 9: ESA SWE Service Network
Expert Service Centers (ESC):
  Solar Weather (BE)
  Heliospheric Weather (UK)
  Space Particle Radiation (BE)
  Ionospheric Weather (DE)
  Geomagnetic activity (NO)
SWE monitoring system:
  SWE space missions
  Ground-based sensors
Portal and users
  Products grouped by services
  https://swe.ssa.esa.int/current-space-weather
SSA Space Weather Coordination Centre (SSCC) located in Belgium
    two line of supports: first SSCC support and Expert Service Center support

## Slide 11: Solar Weather ESC
To provide, implement and support the Solar Weather products
For observation, monitoring, interpretation, modelling and forecasting of Solar Weather conditions with an emphasis on solar (sub-)surface and solar coronal
Solar phenomena analyzed by high-quality data

## Slide 13: Heliospheric Weather ECS
Heliosphere  solar wind and magnetic field
to provide, improve and support the provision of alerts, forecasts and post event analysis of space weather conditions near to the Earth and within the heliosphere (interplanetary mission)
Euhforia forecast
Prototype level and products in federated websites
Solar wind density
Speed STFC, RAL Space (STFC)

## Slide 14: Heliospheric Weather
EUropean Heliospheric FORecasting Information Asset
Data-driven model for Solar Wind and heliospheric weather

## Slide 15: Space Radiation ESC
high-energy ionized particles with different origin (i.e. Galactic cosmic ray, Solar Energetic Particle, Earth’s trapped radiation belt)
  Galactic cosmic rays (p, α, heavy nuclei) flux is constant and modulated by solar activity, problem for high altitude aircraft crew, we are protect on Earth by geomagnetic field
  SEP (mainly p, e-) accelerated by shock waves associated to CME, they are problem as GCR and for EVA of astronauts
  Radiation belts cause problems for spacecraft
Some services are proposed for future

## Slide 16: Ionospheric Weather ESC
IW affects radio systems in communication, space based navigation and remote sensing
Global Navigation Satellite Systems (GNSS, such GPS) could be delayed, refracted and diffracted by the highly variable ionospheric plasma
GNSS is essential tool for safety of life

## Slide 17: Geomagnetic Conditions ESC
Geomagnetic field shows variations on different scales (slow for years and centuries, daily, irregular variations, during magnetic storms)
Geo-magnetometers

## Slide 18: ESA SWE Services
More than 30 services (data, predictions and tools)
Users: Spacecraft design and spacecraft operations
Human spaceflight
Launch operations
Communications and navigation
Airlines and aviation
Pipeline operations
Auroral tourism

## Slide 19: Spacecraft Design
Spacecraft are affected by Space environment and Space Weather:
  degradation, contaminations, radiation damage, thermal changes, interference
  Spacecraft’ systems and sub-systems design need to be studied:
    Shielding requirements
    Thermal control
    Realistic representation in laboratories

## Slide 20
Environment specification: data archive (statistical information*)
In-orbit verification (local information by Proba 2, Herschel/Planck)
Post event analysis for correlating in-situ anomalies of a spacecraft with space weather phenomena at a given time and/or location
Space Weather in the Solar System (The daily space weather bulletin )
*ionising radiation, plasma, microparticles, atmosphere, and UV
CME prediction and counting
Spacecraft Design
Federated products from Solar Influences Data analysis Center (ROB)
Solar Wind Forecast & CME arrival prediction (UKMO)

## Slide 21: Spacecraft Operation
In-orbit Environment and Effects Monitoring
Post-Event Analysis
In-Orbit Environment and Effects Forecast
Mission Risk Analysis
Space Weather in the Solar System

## Slide 22: Human Spaceflight
In-flight Crew Radiation Exposure
Cumulative Crew Radiation Exposure Risk
Increased Crew Radiation Exposure Risk
Federated products from the Center for Space Radiations (UCL)

## Slide 23: Launch Operation

## Slide 24: Transionospheric Radio Link
Near-Real Time TEC Maps
Forecast TEC Maps
Quality Assessment of Ionospheric Correction
Near Real-Time Ionospheric Scintillation Maps
Monitoring and Forecast of ionospheric Disturbances
to present an overview of the current and forecasted ionospheric conditions with the different types of available data (measurement, nowcast, and forecast) at a global or local level
DLR federated
scintillation indices observed at distributed high-rate GNSS receivers

## Slide 25: Space Surveillance and Tracking
SWE affects LEO objects
Atmospheric Estimates for Drag Calculation
Archive of Geomagnetic and Solar Indices for Drag Calculation
Forecast of Geomagnetic and Solar Indices for Drag Calculation
Products such Kp planetary index of geomagnetic activity
current atmospheric, geomagnetic and solar conditions for drag calculation
Credit: NOAA

## Slide 26: Power System Operation
Service to Power Systems Operations (induced currents)
to present an overview of the current and forecasted geomagnetic conditions and heliospheric weather with the different types of available data (measurement, nowcast, and forecast)

## Slide 27: Aviation
Health of aircrews is affected by SWE phenomena
Access to data, model and tools
Alert service

## Slide 28: Resource Exploitation System Operation
Service to RESO

## Slide 29: Pipeline Operation
Pipeline operation service

## Slide 30: Auroral Tourism
Access to Kiruna (Sweden) sky images, archived and in real-time with 1-minute resolution.
Greenland Aurora Nowcast (DTU Center)

## Slide 31
Credit:

## Slide 32: General Data Service
SWE data archive
Latest Data Service
SWE nowcast and forecast products (daily and weekly)
Alert Service

## Slide 33: SWE
From space+ground-based data and data-processing
Supporting
European industry
  Space mission design
  Planned launches, trajectory
  Suggesting ECSS standards
  Tool available under registration
https://swe.ssa.esa.int/

## Slide 34: Service domain
https://swe.ssa.esa.int/

## Slide 35: Expert Centers Data and Tools

## Slide 36: ESA S2P Satellites
VIGIL Mission (M. Castronuovo Lecture)
Smallsats missions
  As part of the Distributed Space Weather Sensor System (D3S)
  The first is Aurora (optical, far-UV and X-ray) observations
  Based on Cubesat in LEO with high TRL
  A demonstrator mission (Aurora-C) followed by a full constellation of 4-5 SmallSats
  Core instrument: Wide Field of View Auroral Imager (WFAI) consisting of two modular assemblies, the Auroral Optical Spectral Imager (AOSI) and the Auroral UV Imager (AUI)

## Slide 37: Long-Term Sustainability (LTS) guideline
Two guidelines address Space Weather
Guideline B.6 - Share operational space weather data and forecasts
Guideline B.7 - Develop space weather models and tools and collect established practices on the mitigation of space weather effects

## Slide 38: Thank you!
Website and manuals
https://swe.ssa.esa.int
https://swe.ssa.esa.int/manuals-and-tutorials

## Slide 39: NASA SWE
https://www.swpc.noaa.gov

## Slide 40: Geomagnetic field and magnetosphere
Credit: SOHO (ESA & NASA)