## Slide 1: Multi-instrument approach to ionospheric studies
Lucilla Alfonsi
lucilla.alfonsi@ingv.it
Eastern Africa Capacity Building Workshop on Space Weather and Low-latitude Ionosphere

## Slide 2
The ionospheric electron density and the height can be derived from radio probing (ground and space-based) exploiting the ionosphere property of influencing the radio wave propagation (by working frequencies spanning from kHz to GHz range).
VHF, HF radars and receivers provide several information on plasma structuring and variability but the devices are sparse and offer poor coverage (in time and space)
L-band (eg. GNSS) is a very powerful diagnostic tool but often does not provide a complete picture in time and space

## Slide 3
In-situ satellite measurements from LEO satellites allow deriving the electron density, electron temperature, ion drift and velocity along the satellite line of sight inside the ionosphere but the satellite moves too fast to provide a good coverage in space and time.
Credits: ESA Swarm
EngineerIT
Notes: The Langmuir probe technique involves applying a voltage to a metallic conductor immersed in plasma and observing the collected current. The observed total current, I, is a summation of various currents such as electron and ion thermal currents, photoelectron current, secondary electron currents, …

## Slide 4
IONOSPHERIC ELECTRON DENSITY FROM LANGMUIR PROBE ON BOARD LEO SATELLITES:
The Swarm measurements
Mission
Launched: 22 November 2013
Duration: 4 years (following 3-month commissioning phase) but still in orbit!
Type: Low Earth; near-polar Configuration: constellation of three identical satellites: two orbit side-by-side, decaying naturally from an initial altitude of 460 km to 300 km over 4 years; the third maintains an altitude of about 530 km.
The final constellation of the mission was achieved on 17 April. Swarm A and C form the lower pair of satellites flying side-by-side (1.4° separation in longitude) at an altitude of about 470 km (inclination angle is equal to 87.35°), whereas Swarm B is cruising at higher orbit of about 520 km (inclination angle is equal to 87.75°).
https://earth.esa.int/web/guest/missions/esa-eo-missions/swarm/mission-overview#Swarm_Mission

## Slide 5
Other useful instruments
Magnetometers
Optical instruments: All Sky Cameras, All Sky Imagers
UV sensors
…
www.space.dtu.dk
sirius.bu.edu

## Slide 6
WHY RELYING ON DIFFERENT MEASUREMENTS?
Detection of perturbation effects on ionosphere
Investigation of the cause-effect mechanisms through post-processing analysis
Gap analysis on what is still missing for a better understanding
ADVANCEMENT OF KNOWLEDGE
IMPROVEMENT IN MODELING
IMPROVEMENT IN ALERTING
IMPROVEMENT IN MITIGATING

## Slide 7
Courtesy J. Damaceno
The combination of different kind of measurements is very informative, but…

## Slide 8
…BUT
Different observation geometry
Different sampling
Different working frequency
Different spatial coverage
Different temporal coverage
Different metrics and standard
…

## Slide 9
Once the case event is decided we know where and when the event is
First step: fill in a checklist
Instrument | Geographic/ Geomagnetic sector (known) | Temporal coverage (known) | Considered (C)/ Not considered (NC)
Ionosondes |  |  | 
Inchoerent Scatter radars |  |  | 
HF-backscattering radars |  |  | 
Ground-based GNSS receivers |  |  | 
Space-based GNSS receivers |  |  | 
In situ LP/TI |  |  | 
SAR |  |  | 
Others?... |  |  | 
www.eswua.ingv.it
An example of checklist

## Slide 10
Instrument | Geographic/ Geomagnetic sector (known) | Temporal coverage (known) | Considered (C)/ Not considered (NC)
Ionosondes |  | X | NC
Inchoerent Scatter radars |  |  | C
HF-backscattering radars | X |  | NC
Ground-based GNSS receivers |  |  | C
Space-based GNSS receivers | X | X | NC
In situ LP/TI |  |  | C
SAR |  | X | NC
Others?... |  |  | 
www.eswua.ingv.it
An example of checklist
Once the case event is decided we know where and when the event is
First step: fill in a checklist

## Slide 11
Phase (a.u.)
L. Alfonsi - An attempt of adaptive phase detrending for GNSS scintillation detection
Some recall:
Ionospheric scintillations: sudden and rapid fluctuations of phase and amplitude of the GNSS signals triggered by ionospheric plasma irregularities due to the diffraction of the signal.
If the signal meets the “irregularities of the ionosphere" the signal may “Scintillate"
How to monitor
An example: the study of the ionospheric irregularities from the GNSS perspective

## Slide 12
What about the irregularities scale-size triggering scintillations on GNSS signals?
Amplitude scintillation:
Diffraction triggered by small-scale irregularities
What does “small” means?
Small for GNSS signals:
scale-sizes up to hundreds of meters
nF: Fresnel’s Frequency
VREL: relative velocity ray-path-ionosphere
dF=sqrt(2*l*hIPP)
l∼19 cm for L1, assuming hIPP = 350 km
dF is about 250 m
Log(PSD)
Log(n)
nFresnel
nNyquist

## Slide 13
The study of the ionospheric irregularities
100 m
1 km
10 km
*from a GNSS perspective
100 km
1000 km
*Small scale
(Fresnel’s scale)
*Medium scale
*Large scale
Credits: Yokoyama
Credits: Cherniak
Credits: NASA
Courtesy Luca Spogli

## Slide 14
Ionospheric irregularities can form due to:
Neutral atmosphere variability
Earthquake, volcanic and tsunami events
Eclipses
Anthropogenic sources
Space weather events
From Jin et al., 2015 (adapted from Kamogawa, 2004)

## Slide 15
Integrated information
GNSS receivers
Ionosonde
Multi-sensor observation
Swarm A/C
CSES / Swarm B
50 km
1000 km
Ionosphere
In-situ information of
the topside ionosphere
Bottom-side ionosphere
information
⁓ 510 km
⁓ 440 km
Magnetometer
Equatorial Electrojet
Ne
foF2
hmF2
TEC
Courtesy Luca Spogli

## Slide 16
Space weather event of September 2017
ionospheric response from low latitudes (India) and high latitudes (Antarctica)
GEOSPACE
EARTH

## Slide 17
Observing system | System output or derived product | Expected Information
GNSS ground-based receivers | DTEC, TEC, scintillation indices | Ionospheric irregularities
Swarm satellites | Ion density | In-situ electron density variations
Ground-based magnetometers | Geomagnetic field components | Geomagnetic field variations
Space weather event of September 2017 - ionospheric response over India

## Slide 19
Highlights of the results from the ground-based magnetometer
Geomagnetic horizontal field variations ΔH at ABG and TIR
Difference between horizontal field variations at ABG and TIR (black curve) and its average regular variation (green strip)
equatorial electric field variation (magenta curve) and disturbed part of the difference between horizontal field variations at ABG and TIR (blue curve).
From 7 September 00:00 UT to 8 September 18:00 UT
  the southward Interplanetary Magnetic Field component Bz
  the Joule heating.
In the early UT hours of 7 September, ΔEEF fluctuations are in phase with those observed in the Δ(ΔH)D, indicating that probably the main disturbance came from PPEF.
From 18:00 (corresponding to ~ 23 LT) onwards fluctuations of both ΔEEF and Δ(ΔH)D are not always in agreement: interplay between PPEF and DDEF effects on EEJ intensity variations. In this time range, main PPEF events peak during local daytime, specifically at 03:55 UT, 06:20 UT, 06:50 UT and 07:15 UT on 8 September.

## Slide 20
From Alfonsi et al., 2021
TEC difference between 8 September and quiet reference
Green diamonds represent the time and latitude of IPP having ROTI>0.5 TECu/min, while black dots are for IPP having S4>0.3.
Absolute TEC from 4 to 9 September 2017
The orange dashed lines indicate the position of the magnetic equator and of the isoclinic lines at +15° and +20°. The blue dashed lines indicate the time of the solar terminator at (24°N; 88°E).

## Slide 21
Is the Nyquist frequency of the ROTI observation (2 x 30 s)-1
A simplified picture…
… so large scales with respect to what revealed by S4
Scale-sizes up to hundreds of meters
From GNSS receivers we can derived ROTI
Adapted from Luca Spogli
?

## Slide 22
Detrended TEC (∆TEC) of the two stations pair NPGJ and LCK3 and of the pair LCK3 and HYDE (quasi-meridionally distributed) between 14:30 UT and 15:45 UT on 8 September for PRN18. In the bottom panels the corresponding cross-correlation coefficient between −45 and + 45 min is reported, while the distance between the IPPs of PRN18, related to the different stations at the same time.
From both the station pairs the mean propagation velocity can be derived from the ratio between the time lag corresponding to the maximum correlation coefficient and the mean distance of the IPPs.
From Alfonsi et al., 2021

## Slide 23
Space weather event of September 2017 - India
From Alfonsi et al., 2021
Time profiles of S4 and of ROTI obtained by considering all GNSS satellites in view from the station indicated in each panel during 7 and 8 September. The red-dashed lines indicate the time of the passage of the Sun terminators at the station location and at an altitude of 120 km and of 350 km. The green shaded area indicates the ranges S4<0.3 and ROTI<0.5 TECu/min.

## Slide 24
From Swarm satellites other scale sizes can be identified
Velocity of Swarm satellites: 7.5 km/s
Sampling frequency of the electron density by onboard Langmuir probes: 2Hz
Maximum resolution of the ionospheric irregularities scale-size:
7.5·103 (m/s) x 0.5 (s) ≈ 4·103 m
By Swarm data analysis we can identified irregularities of few kilometers-scale size or bigger
With faceplate electron density measurements sampled at 16 Hz, the maximum resolution of the ionospheric irregularities scale-size ≈500 m

## Slide 25
INGREDIENTS TO STUDY THE IONOSPHERIC RESPONSE |  | 
Observing system | System output or derived product | Expected Information
GNSS ground-based receivers | DTEC, TEC, scintillation indices | Ionospheric irregularities
Defense Meteorological Satellite Program | Auroral radiance | Auroral oval position
Ground-based ionosondes | ionograms | Ionospheric irregularities/extra-ionization:absorption
Ground-based magnetometers | Geomagnetic field components | Geomagnetic field variations
Swarm satellites | Ion density | In-situ electron density variations
Space weather event of September 2017 - ionospheric response over Antarctica

## Slide 26
From D’Angelo et al., 2021
S4 sensitive to scale-sizes up to hundreds of meters
S4 sensitive to scale-sizes up to hundreds of meters

## Slide 27
Comparison of scintillations from 3 stations
The time-shift in the S4 enhanchement appearance suggest the small scale ionospheric irregularities are moving anti-sunward
D’Angelo PhD thesis, 2018

## Slide 28
From D’Angelo et al., 2021
D’Angelo PhD thesis, 2018
From Alfonsi et al., 2022
Climatological representation of the SANAE GNSS receiver field of view wrt auroral oval position
(black IQ=0; red IQ=6) from the Feldstein model
Polar-view maps in AACGM latitude and MLT of the austral auroral radiance measured by SSUSI instrument at 14:04 UT. The map also reports the auroral oval boundary location retrieved from the auroral radiance data, and S4 greater than 0.1 recorded at SANAE

## Slide 29
nF: Fresnel’s Frequency
VREL: relative velocity ray-path-ionosphere
dF=sqrt(2*l*hIPP)
Computing from working frequencies of few MHz
dF is of the order of 1-10 Kilometers
University of Colorado/KOPRI
What scale sizes of the ionospheric irregularities from vertical sounding?

## Slide 30
From Alfonsi et al., 2022
From D’Angelo PhD thesis, 2018
Ionogram series recorded by Jang Bogo VIPIR between 13:00 and 16:00 UT on September 8, 2017

## Slide 31
Useful References
Alfonsi, L., Cesaroni, C., Spogli, L., Regi, M., Paul, A., Ray, S., ... & Sinha, A. K. (2021). Ionospheric disturbances over the Indian sector during 8 September 2017 geomagnetic storm: Plasma structuring and propagation. Space Weather, 19(3), e2020SW002607.
Alfonsi, L., Bergeot, N., Cilliers, P. J., De Franceschi, G., Baddeley, L., Correia, E., ... & Zou, S. (2022). Review of Environmental Monitoring by Means of Radio Waves in the Polar Regions: From Atmosphere to Geospace. Surveys in Geophysics, 43(6), 1609-1698.
D’Angelo, Investigation of GNSS scintillations under different configurations of the magnetosphere-ionosphere coupling
Thesis for the degree of Doctor of Philosophy, 2018 http://hdl.handle.net/2307/40642
D’Angelo G, Piersanti M, Pignalberi A, Coco I, De Michelis P, Tozzi R, Pezzopane M, Alfonsi L, Cilliers P, Ubertini P. Investigation of the Physical Processes Involved in GNSS Amplitude Scintillations at High Latitude: A Case Study. Remote Sensing. 2021; 13(13):2493. https://doi.org/10.3390/rs13132493

## Slide 32: Multi-instrument approach to ionospheric studies
Lucilla Alfonsi
lucilla.alfonsi@ingv.it
Eastern Africa Capacity Building Workshop on Space Weather and Low-latitude Ionosphere
Thanks!

## Slide 33: Backup slides

## Slide 34
RIOMETER 38.2MHz 26 February 2004
mV
UT

## Slide 35
ADOPTING A GNSS PERSPECTIVE TO APPROACH A MULTI-INSTRUMENT STUDY OF THE IONOSPHERIC IRREGULARITIES
Small scale: scale sizes up to hundreds of meters
What about larger scales?
What about the spatial and temporal evolution of the irregularities (any scale size)?
What about the formation mechanisms?

## Slide 36
METRICS and STANDARD
a common language still missing in the ionospheric community but crucial for space weather
Instrument | Data metrics | Data standard
Ionosondes and Digisondes |  | 
Inchoerent Scatter radars |  | 
HF-backscattering radars |  | 
Ground-based GNSS receivers | X | 
Space-based GNSS receivers | X | 
In situ LP/TI | X | 
www.eswua.ingv.it

## Slide 37
Scintillation indices
Ampl.
50 km
1000 km
Ionosphere
Phase
A simplified picture
Loss of lock
Reduced accuracy of positioning

## Slide 38
Concordia Station - Antarctica
September 2017 storm

## Slide 39
What causes phase and amplitude fluctuations in the GNSS signals?
Ionospheric irregularities
Scale size range: full ionospheric spectrum
Affects: phase
Physical mechanism: phase mixing
Effect: deterministic fluctuations
Mitigation: IFLC (1st ionospheric order)
Positioning issues: Cycle Slips, Losses and Lock, Phase Noise, 2nd order ionospheric effect (fraction of cm), etc.
Scale size range: up to Fresnel’s scale
Affects: amplitude, phase
Physical mechanism: decorrelation, interference
Effect: stochastic fluctuations
Mitigation: e.g., Conker et al., Aquino et al., etc., de-weighting methods.
Positioning issues: stochastic nature is challenging, TEC cannot be calculated
Refraction
Diffraction

## Slide 40
Phase “fluctuations”:
2 mechanisms:
-diffraction (small-scale irregularities)
-refraction (all scale range and scaling with 1/f)
Stochastic and deterministic effects
What is scintillation?
A deeper look
Log(PSD)
Log(n)
Phase Amplitude
ncutoff=nFresnel
nNyquist
If cutoff frequency is “wrong” (ususally fixed at 0.1 Hz), detrending is wrong, sF value includes mainly phase fluctuations due to refraction, i.e., mostly deterministic effects.
Overestimated sF
0.1 Hz
Not suitable at high-latitudes
Notes: By adopting c = F = 0.1 Hz and by considering
hirr = 350 km, the relative velocity is vrel = 36.5 m/s.

## Slide 41
What is scintillation?
Scintillation on L1?
Scintillation on L2?
NO! Ionosphere-Free Linear Combination says NO!
*adapted from a slide by Jayachandran (UNB)

## Slide 42
What is scintillation?
Scintillation on L1?
Scintillation on L2?
YES! Ionosphere-Free Linear Combination doesn’t account for all fluctuations
*adapted from a slide by Jayachandran (UNB)

## Slide 43
What is scintillation?
If properly detrended, SigmaPhi has almost the same information content of S4
Spogli et al. (2021).
IEEE Geoscience and Remote Sensing Letters.
Ghobadi et al. (2020).
GPS Solutions
Courtesy of Jayachandran (UNB)

## Slide 44
Spogli et al. (2021).
IEEE Geoscience and Remote Sensing Letters.
Cesaroni et al. (2021).
Earth and Planetary Physics
This is an issue for high-latitude only, where plasma convection is way larger
0.1 Hz cutoff is not that bad at low latitudes…