## Slide 1: Low-Cost SDR-Based Ionosonde / HF bistatic ionospheric sounder data ingestion into NeQuick 2
A. Kashcheyev1, A. Koloskov1, B.Nava2, P.T. Jayachandran1 and V. Paznukhov3
(1) University of New Brunswick, Fredericton, NB, Canada
(2) The Abdus Salam International Centre for Theoretical Physics, Trieste, Italy
(3) Institute for Scientific Research, Boston College, Boston, MA, USA
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 2
Reduce the cost of ionospheric sounding keeping scientific grade data quality
Replace aging instrument(s)
Reduce level of interference reducing transmitted power
Make instrument portable
Allow developing countries use the technology
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
Motivation

## Slide 3
Digisond DPS-4D
CADI
VIPIR (Dynosonde)
INGV?
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
Ionosonde market

## Slide 4: Low-cost ionospheric sounders
GNU Chirp sounder, Yuha Vierinen (https://www.sgo.fi/~j/gnu_chirp_sounder )
  Software defined radio-based receiver for monitoring ionospheric sounders (ionosondes) and over-the-horizon radars that use linear frequency sweep FM-CW transmissions
  Based on gnuradio and relies on Ettus research USRP2 and USRP N210 based digital receivers
  The receiver can be used to receive the whole HF band (typically at 25 MHz bandwidth) simultaneously, and to receive multiple sounders simultaneously
Design of a flexible and low-power ionospheric sounder, Alex Morris, M.S. Thesis (https://scholarworks.alaska.edu/handle/11122/4535)
  USRP-N200 based ionospheric sounder
  Active magnetic loop antenna
  Peak transmit power 10W
  Barker code
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 5
SDR-based ionosonde (ISDR): core SDR
Software-defined radio (Spartan FPGA-based)
Direct conversion receiver/transmitter
Dual 100 MS/s, 14-bit ADC
Dual 400 MS/s, 16-bit DAC
Up to 50 MS/s Gigabit Ethernet Streaming
UHD interface (open source available via Github)
Supports different daughterboards (in our case they are LFRX and LFTX, 0-30 MHz)
Supports external reference oscillator and PPS signal input (coherent work capabilities)
Ettus research (NI) USRP N200
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 6
ISDR: functional diagram
Basic configuration, single channel
Extended configuration, dual-channel
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 7
Vernadsky Research Base,
Galindez Island
Geographic
-65.25°N 64.26°W
Geomagnetic (IGRF-13)
-51.06°N 9.27°E
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
ISDR: setup

## Slide 8
ISDR: setup
HF RX
LF RX
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 9
IPS-42
SDR-based
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
ISDR: setup

## Slide 10
Comparison Results: examples
ISDR
IPS-42
Dec 2021
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
3.5 kW
100 W

## Slide 11
Comparison Results: examples
Only ISDR
Only IPS-42
Both
ISDR - 4.5km (16-bit code)
IPS-42 - 6km
Scaling soft - 5km
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 12
Comparison Results: statistics
Year 2021
ISDR - 3 min
IPS-42 - 20 sec
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
ISDR - 4.5km (16-bit code)
IPS-42 - 6km
Scaling soft - 5km

## Slide 13
Comparison Results: statistics
Year 2021
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 14
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
Results: publication

## Slide 15
~400m
2022
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
New setup: extended version

## Slide 16
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
New setup: first results

## Slide 17
Research Base “Ak Vernadksy”,
Antarctica (Apr 2017)
Kharkiv, Ukraine (Dec 2017)
Blissville, Canada (Dec 2019)
Abuja, Nigeria (2024?)
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
ISDR network

## Slide 18
USRP N200, LFTX & RFTX - $3,260 USD
https://www.ettus.com/all-products/un200-kit/
ICOM IC-718 - $780 USD
https://www.universal-radio.com/catalog/hamhf/0718.html
Data logger PC - $290 USD
https://www.amazon.com/Beelink-Lake-N100-Mini-Computer-Supports-Home-Server/dp/B0C339KVH9
GPSDO - $140 USD
https://www.aliexpress.com/item/4001022596521.html
Cabling - ~$200 USD
https://www.aliexpress.com/item/4001022596521.html
Total: < $5,000 USD
18
Bill of material
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 19: HF bistatic ionospheric sounder data ingestion into NeQuick 2
A. Kashcheyev1, A. Koloskov1, B.Nava2, P.T. Jayachandran1 and V. Paznukhov3
(1) University of New Brunswick, Fredericton, NB, Canada
(2) The Abdus Salam International Centre for Theoretical Physics, Trieste, Italy
(3) Institute for Scientific Research, Boston College, Boston, MA, USA
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 20
Can signals of opportunities (e.g. from existing ionosondes) be used for scientific research?
Can a simple and a relatively low-cost technique help improving the description of the ionosphere?
Can this data be used in real-time, without a need of manually/automatically scaling?
Are there any practical application of the technique/data?
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
20
Motivation

## Slide 21
Site 1 | Site 2 | Distance, km
Blissville, NB | Newton, MA | 520
Blissville, NB | Midpoint | 260
Blissville, NB | Millstone Hill, MA | 515
Newton, MA | Millstone Hill, MA | 40
 | Site | Location
 | Blissville, NB, Canada (TX & RX) | 45.6 N, 66.6 W
 | Newton, MA, USA (RX) | 42.3 N, 71.2 W
 | Millstone Hill, MA, USA (Digisonde) | 42.6 N, 71.5 W
 | Midpoint | 44.0 N, 69.0 W
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
21
Experiment layout

## Slide 22
Delta antenna (TX)
Horz dipole antenna(s) (RX)
SDR (USRP N-200 + LFTX, LFRX)
GPS disciplined OCXO
Power amplifier (600W max)
30 sec/ionogram
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
22
ISDR (TX & RX)

## Slide 23
Active loop antenna
SDR (USRP N-200, LFRX)
GPS disciplined OCXO
Data logger (PC)
USRP N200 kit
PC (Linux or Windows)
Ethernet 1 Gb
Ethernet 1 Gb
GPSDO
10 MHz + PPS
HF RX antenna
GNSS antenna
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
23
ISDR oblique (RX)

## Slide 24
Blissville Millstone Hill Newton
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
24
Experimental data

## Slide 25
The model profile formulation includes 6 semi-Epstein layers with modeled thickness parameters and is based on anchor points defined by foE, foF1, foF2 and M(3000)F2
These values can be modeled (e.g. ITU-R coefficients for foF2, M(3000)F2) or experimentally derived
Model inputs are: position, time and solar flux; the output is the electron concentration at the given location and time
B. Nava, P. Coïsson, S. M. Radicella, "A new version of the NeQuick ionosphere electron density model", Journal of Atmospheric and Solar-Terrestrial Physics (2008), doi:10.1016/j.jastp.2008.01.015
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
25
NeQuick 2 model

## Slide 26
Az parameters concept is implemented in NeQuick 2
Az(foF2) controls foF2
Az(hmF2) controls hmF2
Alpha(τ) is a factor of the thickness parameters (B2)
B. Nava, S. M. Radicella and F. Azpilicueta, "Data ingestion into NeQuick 2," in Radio Science, vol. 46, no. 06, pp. 1-8, Dec. 2011, doi: 10.1029/2010RS004635
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
26
NeQuick 2 modification

## Slide 27
Kashcheyev, A., B. Nava, and S. M. Radicella (2012), Estimation of higher‐order ionospheric errors in GNSS positioning using a realistic 3‐D electron density model, Radio Sci., 47, RS4008, doi:10.1029/2011RS004976
Numerical 3-D ray-tracing algorithm
Supports different ionospheric models (e.g. IRI, NeQuick 2, parabolic, quasi-parabolic, exponential etc.)
Supports 2 magnetic field models (IGRF, WMM)
Solves for the homing-in problem
NeQuick 2 modified is used
W/O magnetic field
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
27
Ray tracing

## Slide 28
Az(foF2) = 102 sfu, Az(hmF2) = 102 sfu, Alpha(τ) = 1.0
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
28
Climatology

## Slide 29
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
29
Data ingestion

## Slide 30
foF2 error: 0.7 MHz -> 0.1 MHz
hmF2 error: AVG: -80 km -> 12 km; STD: 26 km -> 20 km
Az(foF2) = 138 sfu, Az(hmF2) = 49 sfu, Alpha(τ) = 1.4
foF2 error: 1.1 MHz -> 0.1 MHz
hmF2 error: AVG: -96 km -> 0 km; STD: 48 km -> 22 km
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
Results
30

## Slide 31
Conclusions
Long-term comparison showed ISDR has the same or higher level of performance
Advantages: low-cost, low-power, reliability, flexibility
Disadvantages: longer sounding time
ISDR is recommended to replace IPS-42
A possibility to use higher power amplifier to reduce sounding time is under discussion
31
ICTP Workshop, Malindi, Kenya, October 03-12, 2023

## Slide 32
Bistatic HF ionospheric sounder provides useful data
Data ingestion technique into NeQuick 2 model is implemented
The results of the data ingestion are promising
Extension of the existing sounding network can be achieved at low-cost/low-efforts
Good candidate for improving regional and possibly global description of the ionosphere in 3D
ICTP Workshop, Malindi, Kenya, October 03-12, 2023
Conclusions
32