## Slide 1: Precision measurements of nuclear data for planetary nuclear spectroscopy
Joint ICTP-IAEA Meeting
10/17/2023
Mauricio Ayllon Unzueta

## Slide 2: Our team
Mauricio Ayllon
Ann Parsons
Patrick Peplowski
Jack Wilson
Bernhard Ludewigt
Arun Persaud
Caroline Egan
Richard Starr

## Slide 3
Planetary nuclear spectroscopy allows us to measure the bulk elemental composition of a planetary object
Lunar prospector gamma ray spectrometer: first direct measurements of the lunar chemical composition of the entire surface. Image credit NASA
GRS
NS
GRS = Gamma ray spectrometer
NS = Neutron sensor
Passive orbital measurements
Passive/active in situ measurements
Constrain theories on formation and evolutionary processes.
Identify resources, anomalies, biosignatures.
Provide geochemical context for other instruments.
Plan future missions.
Inspected volume ~ 50 x 50 x 50 cm3

## Slide 4: Notable past missions with nuclear spectrometers
Image credit: Patrick Peplowski (JHU-APL)

## Slide 5
Image credit: Patrick Peplowski (JHU-APL)
Successfully launched last Friday!

## Slide 6: Dragonfly: Mission to Titan
In-situ active GRS:
Pulsed neutron generator (PNG) onboard.
Monoenergetic 14.1 MeV neutrons from DT reaction.
Allows for higher elemental sensitivity with shorter integration times.
Titan, Saturn’s largest moon
Dragonfly mission (2027) will have a PNG, GRS, and a NS onboard.
DraGNS:
Dragonfly Gamma-Ray and Neutron Spectrometer.
Measure bulk composition of Titan surface and provide context for other instruments.
PNG
HPGe + 3He

## Slide 7: Challenge to gamma ray spectroscopy: cross sections
The limiting factors to higher elemental precision are the gaps and inconsistencies in gamma production cross section libraries.
56Fe(n,n’g) @ 847 keV cross section.
27Al(n,n’g) @ 1720 keV cross section.
GEANT4 benchmarking metrics produced by Peplowski [2022] highlighting deficiencies in simulation of neutron-induced gamma-ray production.
None of the libraries yield a 1-𝝈 match to the measurements.

## Slide 8: How are we trying to improve (n,n’g) cross sections? Enter Associated Particle Imaging (API)
LBNL: Arun Persaud, PI
NASA funded work allowed for the first precision measurements of inelastic scattering cross sections with a novel instrument system at LBL: Associated Particle Imaging (API).
API vs. other techniques:
API: Direct flux measurements
Other: Activation foils “gold standard”
API: Only prompt reactions
Other: Difficult to filter out parasitic reactions
API: Monoenergetic neutron flux
Other: Requires additional neutron energy measurements (nTOF, etc.)
API: Gamma-ray background suppression
Other: May be difficult to account for background
API: Compact, portable, low-cost
Other: Usually large facilities e.g. accelerator, reactor

## Slide 9: First measurement campaign (Aug 2022)
Fe
Cu
C

## Slide 10: 56Fe(n,n’g) cross sections
Organization | Year | En (MeV) | σ - 847 keV (mb) | σ - 1238 keV (mb)
This work | 2022 | 14.05 ± 0.09 | 695 ± 5.1% | 339 ± 5.1%
GELINA | 2014 | 14.14 ± 0.14 | 699 ± 4.1% | 356 ± 5.0%
LANL | 2004 | 14.05 ± 0.10 | 705 ± 3% | N/A
ORNL | 1990 | 14.53 ± 0.56 | 621± 4.7% | 290 ± 5.5%
Talys | - | 14.1 | 655 | 333
847 keV
1238 keV
Python based gamma spectroscopy GUI (https://github.com/mauricioAyllon/NASA-gamma).
TALYS:
Used to design experiments.
Predict measurement times, expected energies
Optimize geometry, target mass, etc.
Predict angle dependencies

## Slide 11: Thank you for your attention!
Image credit: NASA (SLS)
Contact: mauricio.ayllonunzueta@nasa.gov

## Slide 12
Extra slides

## Slide 13
Proposed list of isotopes needed for successful space missions

## Slide 14: Angular distributions

## Slide 15: Angular distributions with TALYS
Based on Legendre coefficients and following Baghdad Atlas paper

## Slide 16: Neutron energy distribution

## Slide 17: Neutron energy distribution

## Slide 18: Target thickness selection criteria