## Slide 1
High-Frequency (HF) Vertical Ionospheric Soundings:
Main Features and their Interpretation
Michael Pezzopane
michael.pezzopane@ingv.it
Istituto Nazionale di Geofisica e Vulcanologia, 00143, Rome, Italy

## Slide 2
2003 - Rome
2024 – Gibilmanna (Sicily)
From the very beginning to now……….
me
Enrico
me
Enrico
Claudio
Antonio
Gioacchino

## Slide 3
Tx
Rx
Possible Ionospheric Propagations: Oblique and Vertical
Oblique propagation
Vertical propagation
We will focus
on this method
Increasing the transmitted frequency, in the oblique case we go farther, in the vertical case we go higher.
Anyhow, for both cases there will be a value of the frequency beyond which the signal penetrates the ionosphere without being reflected.

## Slide 4
N is the electron density per unit volume, m the electron mass, e the electron charge and ε0 the electric permittivity of the free space.
fN is called plasma frequency and represents the frequency with which the electrons oscillate around the ions if displaced from their equilibrium position, for instance because of the the perturbing electric field E of the electromagnetic wave propagating through the ionospheric plasma.
A plasma can be considered neutral over temporal scales greater than the corresponding oscillation period τ>>1/ωN.
The Plasma Frequency

## Slide 5
The gyrofrequency is the angular frequency of the circular motion of a charged particle in the plane perpendicular to the magnetic field defined by the following relation:
H is the magnetic field, μ0 the magnetic permeability of the free space, q the charge of the particle, and m the mass of the charged particle.
The Gyrofrequency

## Slide 6
The magnetoionic theory is concerned with the propagation of electromagnetic waves through a magnetoplasma.
Specifically, the reflection of the wave occurs when the ionospheric refractive index is equal to 0  n = 0.
Altar-Appleton
equation
The magnetoionic theory -> the Altar-Appleton equation
plasma frequency
wave frequency
collision frequency
gyrofrequency

## Slide 7
After transmitting through a magnetoionic medium an electromagnetic wave with a certain polarisation, two waves (called ordinary and extraordinary) propagate through it; these two waves have the same frequency, different phase velocity and different polarisation. This phenomenon is called magnetoionic birefraction of the electromagnetic wave into the magnetoplasma.
Simply speaking, a wave with a generic polarisation can be thought as the resultant of two waves;
if the wave propagates through an isotropic medium the two components cannot be observed;
if the wave propagates through an anisotropic medium (as it is the case of a magnetoionic medium) the two components are instead observable.
The Altar-Appleton equation neglecting collisions reflection conditions
→
ord
ext

## Slide 8
Radiowaves of variable frequency are transmitted vertically towards the atmosphere. The ordinary mode of the transmitted wave is reflected from the ionosphere when the transmitted frequency matches the electron plasma frequency:
Depending on the reflection height there will be a definite time delay according to the relation:
The experimental trace is then a plot of the virtual height of reflection vs the transmitted frequency, which is called ionogram.
ordinary
extraordinary
km
Vertical Ionospheric Soundings - Ionograms

## Slide 9
km
MHz
Vertical Ionospheric Soundings - Ionograms
f>fNmax
f≤fNmax

## Slide 10
How the Ionogram trace varies along the day
km
AIS-INGV ionosonde

## Slide 11
Nighttime ionogram
Daytime ionogram
Daytime and Nighttime ionograms
AIS-INGV ionosonde
AIS-INGV ionosonde

## Slide 12
Influence of the geomagnetic field on the ionogram trace
AIS-INGV ionosonde

## Slide 13
Influence of the geomagnetic field on the ionogram trace
AIS-INGV ionosonde

## Slide 14
Basic rules for scaling the most important characteristics
Today we will focus mainly on mid-latitude ionograms but we will see also some equatorial ones. This is because most scalers start dealing with mid-latitude ionograms, and because when compared to high- and low-latitude ones their interpretation is simpler.
RULES
• recognise and scale some of the conventional parameters: critical frequencies of the three ionospheric layers, foF2, foF1, foE and their corresponding heights, h’F2, h’F1, h’E.
First, nighttime ionograms are considered, because they are the least complicated  there is only one layer present.
After looking at nighttime ionograms, daytime ionograms are considered  two/three ionospheric layers are now present.

## Slide 15
The necessary work to obtain the ionospheric characteristics from an ionogram is called “ionogram interpretation or ionogram scaling”.
Till a few decades ago this interpretation was performed only manually by expert operators with a ruler and a pencil.
Now, luckily, there are softwares that help the operators to accomplish this demanding (but valuable) work.
The ionogram scaling
ordinary ray
extraordinary ray

## Slide 16
From the analysis of one ionogram several important characteristics (like the critical frequencies and the heights of the different ionospheric layers) can be found, that have a significant role in the studies concerning ionospheric physics, space weather and related phenomena.
Nighttime ionogram
AIS-INGV ionosonde
Scaling the most important characteristics – Nighttime ionograms
F2
foF2
h’F2 = h’F
Earth
Ionosphere
1X
multiple reflections
Earth
Ionosphere
2X

## Slide 17
From the analysis of one ionogram several important characteristics (like the critical frequencies and the heights of the different ionospheric layers) can be found, that have a significant role in the studies concerning ionospheric physics, space weather and related phenomena.
Daytime ionogram
AIS-INGV ionosonde
Scaling the most important characteristics – Daytime ionograms
F2
F1
E
foE
foF1
foF2
h’E
h’F1 = h’F
h’F2

## Slide 18
Multiple stratifications of the F layer
F2
F2
F1
F1
F3
F3
AIS-INGV ionosonde

## Slide 19
E layer
F1 layer
F2 layer
Night
Day
km
Ne (cm-3)
km
100
200
300
400
500
102
103
104
105
NmF2
NmF1
NmE
Correspondence vertical electron density profile – ionogram trace
AIS-INGV ionosonde

## Slide 20
km
Why electron density maxima of the profile correspond to ionogram cusps?
foE
foF1
foF2
NmE
NmF1
NmF2
AIS-INGV ionosonde

## Slide 21
Different types of sounders
Advanced Ionospheric Sounder-INGV Ionosonde, Italy
Digisonde - Space Science Laboratory, University of Massachusetts, Lowell, USA
Vertical Incidence Pulsed Ionospheric Radar (VIPIR), Boulder, CO, USA
KEL Aerospace’s Digital Ionosonde System IPS-42, Australia
Canadian Advanced Digital Ionosonde (CADI)
VISRC2 - Space Research Center of Warsaw, Poland

## Slide 22
In the last decades, the importance of having real-time ionospheric data for Space Weather purposes has greatly increased. For this reason since 80s much work has been performed to develop computer programs able to automatically scale the ionograms giving as output the standard ionospheric characteristics along with an estimate of the electron density profile.
Although much progress has been made, still today a significant effort is invested to increase the reliability of these programs.
Autoscaling of an ionogram

## Slide 23
multiple reflections
h’F2 = h’F
foF2
Digisonde
Scaling the most important characteristics – Nighttime ionograms

## Slide 24
Scaling the most important characteristics – Nighttime ionograms
h’F2 = h’F
foF2
Digisonde

## Slide 25
h’F2 = h’F
foF2
Digisonde
Scaling the most important characteristics – Nighttime ionograms

## Slide 26
Scaling the most important characteristics – Nighttime ionograms
h’F2 = h’F
foF2
Digisonde

## Slide 27
Scaling the most important characteristics – Nighttime ionograms
h’F2 = h’F
foF2
Digisonde

## Slide 28
Scaling the most important characteristics – Nighttime ionograms
h’F2 = h’F
foF2
Digisonde

## Slide 29
Diurnal evolution of an ionogram
00
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
nighttime
nighttime
nighttime
nighttime
nighttime
sunrise - early morning
sunrise - early morning
late evening - sunset
late evening - sunset
late evening - sunset
nighttime
nighttime
nighttime
nighttime
nighttime
daytime
daytime
daytime
daytime
daytime
daytime
daytime
daytime
daytime
F2
F2
F2
F2
F2
F2
E
F2
F2
F2
F2
F2
F2
F1
F1
F1
F1
F1
E
E
E
E
E
E
F2
F2
F2
F2
F2
F2
F1
F1
F1
F1
E
E
E
E
E
E
F2
F2
F2
F2
F2
F2
E

## Slide 30
The ionogram scaling – sunrise/early morning - late evening/sunset
h’F2 = h’F
foF2
foE
h’E

## Slide 31
h’F2 = h’F
foF2
foE
h’E
The ionogram scaling – sunrise/early morning - late evening/sunset

## Slide 32
h’F2 = h’F
foF2
foE
h’E
The ionogram scaling – sunrise/early morning - late evening/sunset

## Slide 33
h’F2 = h’F
foF2
foE
h’E
The ionogram scaling – sunrise/early morning - late evening/sunset

## Slide 34
h’F2
foF2
foF1
h’F1 = h’F
foE
h’E
The ionogram scaling – Daytime ionograms

## Slide 35
h’F2
foF2
foF1
h’F1 = h’F
foE
h’E
The ionogram scaling – Daytime ionograms

## Slide 36
The ionogram scaling – Daytime ionograms
h’F2
foF2
foF1
h’F1 = h’F
foE
h’E

## Slide 37
The ionogram scaling – Daytime ionograms
h’F2
foF2
foF1
h’F1 = h’F
foE
h’E

## Slide 38
Spread F
Ionograms characterized by spread-F phenomena
AIS-INGV ionosonde
flat reflector
AIS-INGV ionosonde
Notes: Presence of plasma irregularities that causes the reflection of the same frequency at different heights and so with different delay times. Consequently, the trace is not defined, spread.

## Slide 39
Sporadic E layer
Ionograms showing sporadic E layers
The term sporadic E (Es) layer refers to thin (a few km) layer of anomalous values of ionization occurring between 90 and 130 km, whose critical frequency is often very high.
These layers form in the ionospheric dynamo region, when metallic ions of meteoric origin converge vertically, mainly due to vertical shears in the horizontal wind (e.g., Haldoupis, 2011, 2012).
AIS-INGV ionosonde

## Slide 40
Earth
Ionosphere
2X
Earth
Ionosphere
1X
Earth
Ionosphere
3X
Earth
Ionosphere
4X
Ionograms showing sporadic E layers – multiple reflections
AIS-INGV ionosonde

## Slide 41
8:00
8:15
8:30
8:45
9:00
9:15
9:30
9:45
10:00
10:15
10:30
10:45
11:00
11:15
11:30
11:45
Ionograms showing no trace because of absorption - May 2024 Mother’s Day superstorm
11 May 2024
normal propagation
absorption
ionosphere

## Slide 42
The interpretation of a parameter can, if necessary, be qualified by a letter indicating the extent of the uncertainty characterizing the interpretation. A descriptive letter is added to indicate why this reduced level of accuracy has affected your interpretation.
The most used descriptive letters are:
A measurement influenced by, or impossible because of, the presence of a sporadic E layer
C measurement influenced by, or impossible because of, any non-ionospheric reason
F measurement influenced by, or impossible because of, the presence of spread-F echoes
R measurement influenced by, or impossible because of, attenuation close to the critical frequency
S measurement influenced by, or impossible because of, interference
X measurement refers to the extraordinary component
The most used qualifying letters are:
D greater than
U uncertain or doubtful value
Qualifying and descriptive letters

## Slide 43
Qualifying and descriptive letters

## Slide 44
Now it’s your turn!
sporadic E layer (Es)
≃6.7 MHz
Is there a sporadic E layer?
YES

## Slide 45
Now it’s your turn!
Is it possible to validate a reliable
value for foF2?
NO

## Slide 46
Now it’s your turn!

## Slide 47
Now it’s your turn!
Is it possible to validate a reliable
value for foF2?
NO

## Slide 48
Now it’s your turn!
≃12.2 MHz
Is it possible to validate a reliable
value for foF2?
YES

## Slide 49
Now it’s your turn!
≃13.9 MHz
Is it possible to validate a reliable
value for foF2?
YES

## Slide 50
Now it’s your turn!

## Slide 51
Now it’s your turn!
Is it possible to validate a reliable
value for foF2?
NO

## Slide 52
Now it’s your turn!

## Slide 53
Now it’s your turn!
Is it possible to validate a reliable
value for foF2?
NO

## Slide 54
Thank you

## Slide 55
BACKUP SLIDES

## Slide 56
The AIS-INGV ionosonde was installed in Malindi (3.1° S, 40.1° E) in July 2023.
This new installation is extremely important for two main reasons: 1) it fills a gap in terms of data coverage over the African region; 2) it is located within the equatorial ionization anomaly (EIA) and close to its trough.
Hermanus
Grahamstown
Louisvale (stopped JUL 19)
Madimbo (stopped AUG 2019)
Ilorin(stopped NOV 2021)
Malindi (6.48 S; 111.94 E)
operating since August 2023
Blue dashed curves depict the QD magnetic parallels. (modified from Pignalberi, Pietrella & Pezzopane, 2021)
Before the NORISK project 5 ionosondes (digisondes) were installed in the African continent. Only 3 of them are operational.
The AIS-INGV Malindi ionosonde

## Slide 57
h’F = 366 km
h’F = 357 km
Considered period: hourly ionograms from August 2023 to July 2024 for which the virtual height of the base of the F layer (h’F), when possible, was manually validated through the Interpre software (Pezzopane, 2004).
Importance of ionosonde stations – Estimation of the plasma vertical drift

## Slide 58
The apparent vertical F-layer drift, inferred from ionosonde measurements as Δ(h'F)/Δt is, as theoretically predicted (Bittencourt and Abdu, 1981) and experimentally verified (e.g., Batista et al., 1986), representative of the vertical ExB plasma drift velocity only around the times of pre-reversal vertical drift enhancements, when the layer is high (around 300 km or more).
For smaller heights, the apparent vertical velocity starts to depart significantly from the vertical ExB drift velocity, because of the increasing dominance of the recombination process at these lower heights.
According to the literature, the time window considered reliable is: 12:30 – 19:00 UT
12:30 – 19:00
12:30 – 19:00
12:30 – 19:00
(Fejer et al. (2008) model)
(Fejer et al. (2008) model)
(Fejer et al. (2008) model)
Importance of ionosonde stations – Estimation of the plasma vertical drift

## Slide 59
Importance of ionosonde stations – Estimation of the plasma vertical drift

## Slide 60
negative ionospheric phase
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics at different latitudes.
Importance of ionosonde stations - May 2024 Mother’s Day superstorm
INGV Ionospheric portalhttp://eswua.ingv.it/
Malindi

## Slide 61
Importance of ionosonde stations - May 2024 Mother’s Day superstorm
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics at different latitudes.
negative ionospheric phase
INGV Ionospheric portalhttp://eswua.ingv.it/
Rome

## Slide 62
They are essential for monitoring the ionospheric plasma in real time for Space Weather purposes and to better understand the ionospheric storm dynamics.
Importance of ionosonde stations – effects of the solar eclipse