## Slide 1
ICTP–IAEA 2026
1
TINYML · RADIATION SENSING · EMBEDDED INFERENCE
A tiny model reconstructs distorted radiation pulses
Domain priors · INT8 · no_std Rust · residual-based fallback
Esen Rakhmanov
ICTP–IAEA Workshop 2026 · Bishkek, Kyrgyzstan
DISTORTED MEASUREMENT
RECONSTRUCTED PULSE
256 samples / window

## Slide 2
02
THE PROBLEM
ICTP–IAEA 2026
2
Distortion destroys pulse morphology
Recover the underlying pulse from a fixed 256-sample measurement window.
CLEAN PULSE
DISTORTED MEASUREMENT
noise
baseline drift
pile-up
QUESTION
Can a tiny model
recover the pulse
from the distortion?
x: distorted signal →
y: clean target

## Slide 3
03
WHY EDGE
ICTP–IAEA 2026
3
The model has to fit the edge
Local inference means small memory footprint, integer-friendly computation, and a fixed execution path.
1,473
parameters
256
samples / window
INT8
inference representation
no_std
Rust runtime
TARGET PLATFORM CLASS
ARM Cortex-M-class MCU
Boundary of the evidence
No physical MCU benchmark yet: latency, RAM and energy remain unmeasured on target hardware.

## Slide 4
04
CORE IDEA
ICTP–IAEA 2026
4
Learn the pulse. Regularize the shape.
The CNN learns reconstruction; soft domain priors bias the morphology.
ℒ = ℒMSE + λ₁ℒNonNeg + λ₂ℒArea + λ₃ℒMonotonic
NON-NEGATIVE
Penalize negative predicted amplitude.
AREA
Match reconstructed pulse area.
MONOTONIC TAIL
Suppress upward tail oscillations.
Soft priors — not hard physical constraints.

## Slide 5
05
MODEL
ICTP–IAEA 2026
5
1,473 parameters. Nothing more.
A fixed-window 1D CNN keeps the inference graph deliberately small.
96
Conv 1
1,296
Conv 2
81
Output
1,473
Total parameters
256 input samples → 256 reconstructed samples — single-channel fixed-window reconstruction

## Slide 6
06
RESULT · ABLATION
ICTP–IAEA 2026
6
Area consistency wins — by only 1.6%
Canonical single-seed ablation; RMSE is the common post-hoc metric.
monotonic
0.02177
full
0.02166
baseline
0.02157
nonneg
0.02152
area
0.02122
Interpretation
0.02122
best nominal RMSE
≈ 1.6% lower than baseline
Keep the claim small
All five configurations are within ≈2.6% RMSE. This is a small, configuration-dependent effect — not a universal win.

## Slide 7
07
RESULT · QUANTIZATION
ICTP–IAEA 2026
7
INT8 costs 7.04% RMSE
Fair comparison: same 25-epoch budget, same evaluation set.
FP32-equivalent
0.03502
→
INT8
0.03749
+7.04%
RMSE increase
What this buys
Integer-oriented deployment with a fixed embedded inference path.
Fair-QAT checkpoint
separate from the deployment checkpoint used for safety calibration
Single-run QAT variance is not characterized.
PeakAmpErr 0.20139 → 0.22486
PeakTimeErr 3.916 → 4.789

## Slide 8
08
DEPLOYMENT
ICTP–IAEA 2026
8
No Python in the inference path
Training stays in Python; deployment becomes a small, deterministic Rust runtime.
PYTHON
PyTorch / QAT
INT8 MODEL
quantized weights
MANIFEST
scales + zero-points
RUST
no_std runtime
MCU CLASS
Cortex-M target
no_std
no OS dependency in runtime
INT8
integer-oriented inference
[u8; 256]
fixed-size input / output
Inference path is designed to avoid dynamic allocation; parsing/tooling remain outside the hot path.

## Slide 9
09
DEPLOYMENT · VERIFICATION
ICTP–IAEA 2026
9
Python and Rust agree exactly — on the tested vector
The quantized I/O path is compared in the uint8 domain.
CANONICAL INPUT
PYTHON
RUST
UINT8
OUTPUTS
MAX ABS ERROR
0
MAE = 0
1 canonical vector
Scope of the claim
Bit-exact for the tested canonical vector. This is a deterministic parity smoke test, not statistical validation over the full input distribution.

## Slide 10
10
DEPLOYMENT · TRUST BOUNDARY
ICTP–IAEA 2026
10
When the model should not be trusted, stop using it
A quantized residual becomes an operational decision.
INPUT
TinyPulseCNN
RESIDUAL
RMSE > 54.80?
ACCEPT
CNN OUTPUT
TRIGGER
SMOOTHING FALLBACK
54.80
uint8-domain threshold
p95 of 1,000-sample calibration set
Engineering monitor — not a formal safety guarantee.

## Slide 11
11
RESULT · ROBUSTNESS
ICTP–IAEA 2026
11
The gate is selective — not universal
Observed trigger percentages: 1 held-out ID baseline + 4 synthetic OOD stress regimes.
High noise
100%
Amplitude shift
97%
Massive drift
82.5%
Severe pile-up
0.5%
In-distribution
0%
The important caveat
0.5%
pile-up trigger rate
The residual metric does not separate this regime well.
Statistical scope
N = 200 per regime. These are observed sample percentages, not OOD accuracy, recall, or population false-positive-rate estimates.

## Slide 12
12
CONCLUSION
ICTP–IAEA 2026
12
What we actually demonstrated
01
TINY
1,473 parameters on a 256-sample window.
02
EMBEDDED
INT8 + no_std Rust + max absolute error = 0 on the canonical test vector.
03
HONEST
Selective residual monitoring with known blind spots — especially severe pile-up.
Boundary
Synthetic evaluation · single-seed evidence · no physical detector data · no target-MCU performance benchmark.

## Slide 13
13
LIMITATIONS
ICTP–IAEA 2026
13
What remains unvalidated
Physical detector data
Current results are synthetic; experimental detector waveforms are future work.
Multi-seed robustness
Ablation and fair-QAT results are single-run; variance is not characterized.
MCU performance
No target-hardware latency, RAM or energy benchmark has been measured.
General OOD coverage
The residual gate is selective and demonstrably weak on severe pile-up.
The claims are deliberately narrower than the ambitions.
Next: physical detector data · multi-seed study · real Cortex-M benchmark

## Slide 14
ICTP–IAEA 2026
14
TINY · EMBEDDED · HONEST ABOUT LIMITS
Thank you
Questions
Esen Rakhmanov
ICTP–IAEA Workshop 2026 · Bishkek
github.com/nidara-duo/2026-ictp-iaea
distorted
reconstructed

## Slide 15
BACKUP
Detailed evidence for Q&A
Architecture · dataset · OOD matrix · QAT discrepancy · limitations

## Slide 16
B1
BACKUP · RUNTIME
ICTP–IAEA 2026
B1
Why Rust? The relevant argument is determinism.
Language-level rationale only — no target-hardware benchmark is claimed.
Property | Python | Go | C++ | Rust
GC / runtime pauses | N/A | Yes | No | No
Memory safety | Managed | Yes | Manual | Compile-time
Deterministic lifetime | No | Limited | Yes | Yes
no_std path | No | No | Yes | Yes
Why Rust here
Memory-safe systems language with a no_std path and deterministic object lifetime.
Honest caveat
Rust does not replace measurement: target-hardware timing, RAM, flash and energy still need to be benchmarked.

## Slide 17
B2
BACKUP · DATASET
ICTP–IAEA 2026
B2
Canonical synthetic-data protocol
Parameter | Value | Source
Window | 256 | configs/train.yaml
Training samples | 5000 | configs/train.yaml
Evaluation samples | 1000 | configs/train.yaml
Seed | 42 | Results Freeze MANIFEST
Distortions | noise, sine drift, pile-up, symmetric ±1.0 clip | src/data/generator.py
Scope
Synthetic stress-test generator. No claim of complete physical-detector realism.
Split
5,000 train + 1,000 held-out evaluation. No separate third test split in the canonical freeze.

## Slide 18
B3
BACKUP · OOD MATRIX
ICTP–IAEA 2026
B3
Full robustness matrix: 1 ID + 4 OOD stress regimes
Run | In-Dist. | High Noise | Pile-up | Massive Drift | Amp Shift
baseline | 0.0121 | 0.0660 | 0.0484 | 0.4316 | 0.2147
nonneg | 0.0121 | 0.0659 | 0.0483 | 0.4295 | 0.2140
area | 0.0118 | 0.0695 | 0.0466 | 0.4366 | 0.2191
monotonic | 0.0121 | 0.0655 | 0.0485 | 0.4317 | 0.2130
full | 0.0123 | 0.0702 | 0.0462 | 0.4375 | 0.2186
No single configuration dominates all five regimes.
These are synthetic stress regimes, not physical detector validation.

## Slide 19
B4
BACKUP · QAT DISCREPANCY
ICTP–IAEA 2026
B4
Why are there two INT8 RMSE values?
They come from two deliberately separated QAT stories.
PHASE 1A · DEPLOYMENT
0.02024
INT8 RMSE
FP32 0.02217 → INT8 0.02024
Deployment checkpoint used by the safety chain.
FAIR QAT · SAME 25-EPOCH BUDGET
0.03749
INT8 RMSE
FP32-equivalent 0.03502 → INT8 0.03749
Methodologically fair quantization comparison.
The gap is large and uncharacterized. No multi-run variance study exists.

## Slide 20
B5
BACKUP · LIMITATIONS
ICTP–IAEA 2026
B5
Known boundaries of the evidence
Topic | Current boundary
Synthetic data | No physical detector waveforms yet.
Single seed | No cross-seed variance estimate.
QAT variance | 0.02024 vs 0.03749 discrepancy is uncharacterized.
MCU benchmark | No target-hardware latency / RAM / energy measurement.
OOD coverage | Residual gate is selective and weak on severe pile-up.
Checkpoints | *.pth files are not versioned in the repository.
Research prototype, not hardware-validated production deployment.