## Slide 1: Design and operation of accelerator chain and storage rings
Simone Di Mitri
Elettra Sincrotrone Trieste
University of Trieste, Dept. of Physics

## Slide 2: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 3
photon energy  spatial resolution
L. De Broglie
W. Heisenberg
Why do we need X-rays?
EUV and X-rays are ideal probes of chemical bonds, where most of science is rooted. They can be used to visualize proteins structure, molecular dynamics, atomic levels and orbitals…
Proteins
Atoms

## Slide 4
FLUORESCENCE
EXAFS, XRF
ABSORPTION
Spectroscopy, EXAFS, XANES
SCATTERING
SAXS
DIFFRACTION
Cristallography
e- PHOTO-EMISSION
electronic structure
High energy electrons
Strong magnetic field
SRLS = storage ring light source
How do we generate and use X-rays?
Courtesy J. Als-Nielsen, D. McMorrow

## Slide 5
Almost all experimental techniques gain from a large 6-D photon density, or brilliance (also, spectral brightness)
COUPLING:
Diffraction Limit
This drives the race to 4th generation synchrotron light sources, for ultra-low emittance, matched beams.
Why accelerator-based light sources?

## Slide 6: The importance of being brilliant
is a conserved quantity in a perfect optical system. However, a real beamline includes slits, mirrors, gratings, etc. for manipulation of the light pulse. They show geometrical and surface imperfections, which are stronger for larger spatial and angular footprint of the light on the optical elements.
Courtesy A. Bianco
Courtesy B. Diviacco
Machine design at the state-of-the-art is a good investment because the higher the brilliance at the source is, the higher the brilliance at the sample is!

## Slide 7
Development of SRLS

## Slide 8: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 9
Accelerator size
The beam energy roughly sets the SRLS size:
The e-beam energy determines the photon energy range:

## Slide 10: Dispersion function
High energy electrons on a circular path:
+…
Dispersion function:
Path length and revolution frequency difference, per unit of energy deviation:
“MOMENTUM COMPACTION”
“SLIP FACTOR”

## Slide 11
Synchrotron oscillations
PILL-BOX (standing-wave):
“RF bucket”
“RF acceptance”

typically,
(zero-current limit)
typically,
Synchrotron oscillations:
RF cavities replenish the energy lost every turn  beam energy is constant on average in a turn:

## Slide 12: Filling pattern: “multibunch”
1.5 - 8 GeV, 200 – 500 mA, 100 – 1000 bunches per turn
10 – 50 photon beamlines operating simultaneously
> 5000 hours per year (24h, 7/7 ), 1000 hours reserved for machine physics
> 1000 users / year
Triv  1 – few µs
Shorter photon pulses can be produced in dedicated schemes of few bunches, or with advanced e-beam manipulations.
RF field imposes a synchronization with the particles’ arrival time:
  The harmonic number h is the max. number of “spaces” to be filled (RF buckets)
Adapted from NGLS CDR

## Slide 13: Filling pattern: “hybrid”
~1014 ph/sec/0.1%bw
@sample
~41011 ph/sec/0.1%bw
~3105 ph/pulse/0.1%bw
@sample

## Slide 14: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 15: Strong focusing
Vacuum chamber (Al, Cu, Steel) at ultra-low pressure (< 10-9 mbar), to avoid gas-scattering
Particle beam must be kept in!
 external magnetic focusing
300 MV/m !
1 Tesla…
Normalized quad strength:
Courtesy I. Cudin

## Slide 16: Betatron motion
focal length
Alternated focusing and defocusing quads can provide effective focusing, i.e. stability, simultaneously in both planes.
Hill’s eqs. (pseudo-oscillators) assume linear motion & no frictional forces:
Betatron tune = # oscillations per turn
Emittance:

## Slide 17: Nonlinearities
Particles at (slightly) different energies are focused differently – linear chromaticity:
effect enhanced by many strong quads
Magnets’ misalignment and field errors “resonate” with rational tunes – resonances can lead to beam loss!
Sextupole magnets correct the chromaticity, but at the cost of higher order aberrations!
effect enhanced by many dipoles

## Slide 18: Radiation Damping, Quantum Excitation
Radiation quanta emitted with small but non-zero angle. Total momentum of electrons is reduced.
RF cavities restore the longitudinal momentum only. Transverse divergence of electrons is reduced.
Average variation of oscillation amplitude2 in a turn:
Characteristic damping time:
Radiated power & dispersive motion

## Slide 19: Equilibrium emittance
This is driving world-wide upgrades to multi-bend lattices (4th generation). Radiation is far more collimated and more intense – higher “brilliance”!
damping times

## Slide 20: Liouville’s theorem
The dynamics of a non-dissipative system obeys Hamilton’s equations:
The phase space area (hyper-volume) in proximity of an orbit is a constant of motion.
A storage ring is not a Hamiltonian system because of radiation emission and acceleration.
However, it behaves as if it were a Hamiltonian system.
 The “phase space” emittance is a constant of motion
A storage ring is not a linear system because of high order magnetic field components.
However, it behaves as a linearized system.
 The “statistical” emittance is a constant of motion

## Slide 21: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 22
From relatively sparse to tight, dense, strong focusing lattices
Complex dipoles with transverse and/or longitudinal gradients
Combined multipole magnets
Fringe-field interference
3-D “AI”-driven optimization of magnets design
COMPLEX BEND
DIPOLE–QUAD
Courtesy I. Cudin, G. Le Bec, T. Shaftan
Multi-bend lattices

## Slide 23
4th generation:
MBA + RB
3rd generation: DBA, TBA
10-5
10-6
10-7
10-8
10-9
10-10
Higher Eph
magnets
technology
Courtesy L. Hoummi
Emittance landscape

## Slide 24
Stronger field by shorter poles
Shorter poles permit lower beam energies
technological challenge
energy & cost saving
Compact
APPLE-X
Cryogenic
Superconducting
HTS
Courtesy B. Diviacco, H. Tarawneh, M. Valleau, S. Casalbuoni, M. Calvi
Undulators

## Slide 25
4th generation SRLS are running already!

## Slide 26
…and more are coming!
Upgrade plans ongoing also in UK, Germany, France, Spain,…

## Slide 27: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 28: e-Beam lifetime
Due to physical or dynamic boundaries, the beam current decreases exponentially with time.
  Top-up = frequent refill to keep the current constant, beam is more stable, and thermal drift of components is minimized
Quantum lifetime:
Gaussian
Gaussian w/ cut
Touschek lifetime:
Dynamic aperture:

## Slide 29: Injection chain
Thermoionic gun + RF buncher + linac (“injector”):
  high charge, single bunch or
  low charge, train of bunches
   100 MeV
Booster ring:
  energy ramp to GeV scale (magnets, RF)
   Hz rep. rate
  emittance control for injection efficiency
Booster-to-Storage ring transfer line:
  dc and pulsed electro-magnets for injection
  optics matching
  collimation and diagnostics
Courtesy of SOLEIL

## Slide 30: Injection: Ring-driven
Structured synchronization system is essential to satisfy diverse fill pattern in the storage ring
  single or few bunches, trains, alternated bunches, etc.
Large variety of injection schemes, exploring 6-D separation of stored and injected beam, and eventually coalescence in a damping time or so.
  Transverse separation
  Energy/phase separation
  Swap-out (on-axis beam out–beam in)
Stored beam should not be disturbed by injection.
  Tiny beams in DLSRs make this a challenge.
  Sub-m accuracy in orbit control
Courtesy A. Carniel
Courtesy R. Bartolini, P. Tosolini

## Slide 31: Injection: Linac-driven
High energy e-linacs provide short, low emittance beams, well suited to high injection efficiency.
  Often shared with FELs.
PAL
MAX IV
SACLA

## Slide 32: Outline
Conclusions
Motivations to Synchrotron Light Sources
Beam Energy
Magnetic Lattice
Diffraction-Limited Storage Rings
Accelerator Chain

## Slide 33: Light sources
Brightness
Accelerator-based light sources are the most brilliant sources on Earth, largely coherent.
Other strong points are polarization, repetition rate and diversified radiation sources at SRLS.
Light sources drive technology: RF, magnets, ultra-vacuum mechanics, lasers.
Light sources are multi-purpose science drivers. No one ideal source: pick the one most suited to your experiment!

## Slide 34: Strong points of SRLS
Synchrotrons provide light up to tens of beamlines simultaneously, each beamline receiving light from a dedicated insertion device.
Large flexibility in tuning or selecting radiation wavelength and intensity. Spectrum from IR to hard x-rays.
High average radiation power at the expense of low peak power (incoherent emission) and long pulses (several 10s ps).
Extremely stable.
Now approaching transverse coherence in X-rays.

## Slide 35: Promises of DLSR
Reduction in the source emittance, thus increase in brilliance, will lead to:
significant gain in the emitted or transmitted signals from the samples;
reduced acquisition time for all types of spectroscopies and x-ray scattering techniques;
implementation of photon-hungry techniques such as: high pressure experiments with anvil cells and dilute samples, and spin-resolved ARPES;
improvement of the lateral resolution with focusing optics down to a few-nm scale (e.g. nano-PES, nano-ARPES)
Higher degree of transverse coherence will open unique opportunities for:
Coherent Diffraction Imaging (CDI) with chemical specificity
Ptychography
X-ray photon correlation spectroscopy (XPCS)

## Slide 36
What does the future look like?

## Slide 37: Bibliography
S. Di Mitri, Fundamentals of Particle Accelerator Physics, Springer (2023)
Cern Accelerator School, Yellow Books (1994, 2024) – online
USPAS lectures by W. Barletta – online

## Slide 38: Thank you for your attention Questions are very welcome

## Slide 39: Accelerator science is expanding
Accelerators contributed to Nobel in Physics on average every 3 years (1950 -)
Cyclotron:
artificial radioactive elements
Synchrotron:
-neutrino, CP violation, J/, etc.…
Light Sources: viruses, new materials, planetary processes,…
Circular colliders: Standard Model and beyond

## Slide 40: Synchrotron radiation
Synchrotron radiation is e.m. energy de-coupled from a charge by centripetal acceleration. For example, an ultra-relativistic electron in a magnetic dipole field.
e-bunch
Synchrotron radiation
Bunch self-field
Courtesy of
A. Novokatsky

## Slide 41: Degeneracy parameter
The fraction of spectral flux transversally coherent is the one emitted by a source at, or below, the diffraction limit:
The number of photons transversally and longitudinally coherent is:
Number of photons in the “coherent volume”
It is more difficult to get full coherence at shorter wavelengths
Coherence of radiation  in-phase photons  more effective light-matter interaction

## Slide 42: Transverse coherence
Interference fringes
Collimated, monochromatic light
Phase-correlated field
Classical model: path length over which two waves become out of phase
Uncertainty Principle: the smallest phase space area occupied by the light pulse
Minimum transverse phase space area (“emittance” ) of a transversally coherent light pulse

## Slide 43: Bunch length
Intrabeam scattering (multiple small angle events) enlarges the emittances through diffusion, in proportion to the 3D charge density.
  Mitigated through higher harmonic RF cavity, used to flatten the beam longitudinal phase space and make 3–10  longer bunches.
    Still, (sub-)ps X-ray pulses are being considered. Flux and transparency to standard operation remain a challenge.
I. Martin, PhD Thesis (2011)
S.C. Leemann, PRST-AB 17, 050705 (2014)