## Slide 2
Bending magnets and insertion devices
Gaël LE BEC
4th ICTP School on Synchrotron Light Sources and their Applications
January 13th, 2026

## Slide 3
Introduction to synchrotron radiation
Bending magnets and wigglers
Undulators
Technology

## Slide 4
Introduction to synchrotron radiation

## Slide 5: Introduction to synchrotron radiation
What is synchrotron radiation?
Electromagnetic radiation
Emitted by relativistic charges accelerated in a magnetic field
First observed with 70 MeV electrons on a synchrotron1 in 1947, so its name
The synchrotron radiation is collimated, i.e. emitted in a narrow angle, and tangent to the particle’s trajectories
It is a has a high energy, typically in the keV range and up to a few hundreds of keV for bending magnet radiation
1A synchrotron is an accelerator where the field of the magnets is synchronized with the acceleration of the particles.

## Slide 6: Introduction to synchrotron radiation
Special relativity
The coordinates in two different frames, moving at constant velocity, are linked by the Lorentz transformation:
where is the Lorentz factor, i.e. the ratio of the particle mass to its rest mass.
For an electron with energy :
For 6 GeV electrons (ESRF, APS-U):
(velocity along the direction)

## Slide 7: Introduction to synchrotron radiation
Emission angle
The synchrotron radiation is emitted in a cone with a narrow aperture
For 6 GeV electrons,
Lorentz transformation

## Slide 8: Introduction to synchrotron radiation
Retarted time
The radiation observed at time was emitted earlier, the delay corresponding to the propagation time
The corresponding emission time is called the retarted time. It is linked to the observation time by . After differentiation:
where is a normal vector from the particle to the observer, is the particle velocity and is the speed of light.
Electron
Observer
(See [Feynman, 1963] for a deeper introduction to the retarted time.)

## Slide 9: Introduction to synchrotron radiation
A simple case: retarded time for on-axis observation
The observer time varies with
where is the Lorentz factor, i.e. the ratio of the particle mass to its rest mass.

## Slide 10: Introduction to synchrotron radiation
Retarted time (s)
Observer time (s)
Retarded time in an undulator

## Slide 11: Introduction to synchrotron radiation
Retarded fields and potential
The exact expression of the retarded potentials was published before the discovery of the special relativity and photons!
A. Liénard, 1898
E. Wiechert, 1901
This is the so-called Liénard-Wierchert potential,
or retarded potential

## Slide 12
Bending magnets and wigglers

## Slide 13: What are bending magnets?
Charged particles in an electro-magnetic field
The Lorentz force is:
A magnetic field exert a force which is
Perpendicular to
Perpendicular to the velocity v: the trajectory is bent
In a bending magnet, the particles are accelerated in the transverse direction: radiation is emitted

## Slide 14: What are bending magnets?
Bending magnets in accelerators
Bending magnets are used in accelerator rings
They ensure a close trajectory for the particles
They radiate a high power as synchrotron radiation
ESRF storage ring power
Bending magnets radiation
Undulator radiation
Others

## Slide 15: What are bending magnets?
Dipole magnets
Bending magnets typically have an homogeneous field
This is done by two magnetic poles, i.e. a magnetic dipole
For this reason bending magnets are also called dipole magnets
Bending magnets at the ESRF-EBS
More than 200 bending magnets
These magnets are low field. This ensure a low emittance
Some of bending magnets are also focusing magnets
N
S
ESRF bending magnet

## Slide 16: Bending magnet radiation: critical energy
Light pulse duration
The observer starts to see the radiation emitted at retarted time
The radiation emitted after retarted time is not seen by the observer

## Slide 17: Bending magnet radiation: critical energy
Light pulse duration
During the time , the electron trajectory is bent by an angle
The observer time is linked to the retarded time by
with
Radius

## Slide 18: Bending magnet radiation: critical energy
Light pulse duration
This gives the pulse duration for the observer:
The so-called critical frequency of the radiation is
and the critical energy of the photons is
( is the Planck’s constant and the bending radius)

## Slide 19: Bending magnet radiation
Radiated power
For a relativistic electron on a circular orbit:
This explain the large size of the high energy accelerators!
Energy
Bending radius
Magnetic field

## Slide 20: Bending magnet radiation
Radiated spectrum
1.7

## Slide 21: Bending magnet radiation
Radiated power density
Uniform in the horizontal plane
Collimated within in the vertical plane
Radiated power density of a magnet at , for electrons

## Slide 22: Bending magnet radiation
Polarization
In the symmetry plane, the polarization is purely linear
circular polarization appears out of plane (think about a circular electric dipole to be convienced)

## Slide 23: Bending magnet radiation
Linear pol.
Circular pol.
Circular pol. rate
Linear pol. rate
Polarization
(Figure from [R. Walker, 2003])

## Slide 24: Wigglers
Main ideas
Stack a few bending magnets to increase the photon flux
Alternate the magnet polarities to wiggle around a straight line

## Slide 25: Wigglers
Radiated spectrum
Flux
Poles
Note: the interferences between periods are neglected here.
This is not true at low energy, but wigglers are typically used at high energy

## Slide 26: Wigglers
Deflection parameter
Let’s assume a sinusoidal magnetic field:
( is the undulator period)
We integrate to get the transverse velocity, assuming , and we deduce the angle :
is the so-called deflection parameter. It has a tremendous importance in wiggler and undulator radiation. For wigglers, we typically have .

## Slide 27: Wigglers
Radiation power density
Radiated power density for wiggler with , and electrons, obserbed at

## Slide 28
Undulators

## Slide 29: Undulators
Undulators vs wigglers
Undulators and wigglers are similar devices
Undulators benefit from period to period interferences
This is a wiggler

## Slide 30: Undulators
Undulators vs wigglers
Undulators and wigglers are similar devices
Undulators benefit from period to period interferences
This is an undulator

## Slide 31: Undulators
Undulators vs wigglers
Undulators and wigglers are similar devices
Undulators benefit from period to period interferences
In practice, planar devices with are wigglers
Undulators typically have
This is an undulator

## Slide 32: Undulators
Resonance condition
Average longitudinal velocity:
Electron’s velocity:
by definition of the Lorentz factor

## Slide 33: Undulators
Resonance condition
Average longitudinal velocity:
at

## Slide 34: Undulators
Resonance condition
at
Average longitudinal velocity:
On-axis resonance
Electron to photon distance after one period

## Slide 35: Undulators
Resonance condition – off-axis
Undulator resonance
The wavelength can be tuned with
The wavelength increases off-axis

## Slide 36: Undulators
Resonace condition – off-axis
Energy
Beam size
Resonance
Detuned

## Slide 37: Undulators
Resonace condition – fully tunable undulators
An undulator is fully tunable from the 1st to the 3rd harmonic if
With , we obtain the full tunability . However, means no deflection, i.e. no radiation!
In practice, the full tunability is achieved with . For this reason, undulators typically have .

## Slide 38: Undulators
Undulator spectrum
The on-axis photon angular spectral flux varies with
For more details, see [Walker, 1998] or [Elleaume, 2003]

## Slide 39: Undulators
Undulator spectrum
The on-axis photon angular spectral flux varies with
For more details, see [Walker, 1998] or [Elleaume, 2003]
: fundamental frequency
: number of periods
zeros for with
Linewidth:
1
5
periods

## Slide 40: Undulators
Undulator spectrum
The on-axis photon angular spectral flux varies with
For more details, see [Walker, 1998] or [Elleaume, 2003]
1
3
4

## Slide 41: Undulators
Undulator spectrum

## Slide 42: Undulators
Undulator spectrum

## Slide 43: Undulators
Undulator spectrum
1
3
5
7
9
Photon flux (ph/s/0.1%bw)
Photon energy (keV)
long, , , on-axis, filament beam

## Slide 44: Undulators
Spectral flux through slits
Slits
Off-axis photons have lower energy
This broadens the spectrum peaks!
Integration on finite slits

## Slide 45: Undulators
Spectral flux through slits – fundamental
long, , , on-axis, filament beam
Photon flux (ph/s/0.1%bw)
Photon energy (eV)
Angular aperture

## Slide 46: Undulators
Radiation patern at resonance
Photon energy (keV)
Photon flux
Flux at the 3rd harmonic resonace wavelength

## Slide 47: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam

## Slide 48: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam

## Slide 49: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam

## Slide 50: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam

## Slide 51: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam

## Slide 52: Undulator
Tuning curves
Photon energy (keV)
Photon flux (ph/s/0.1%bw)
long, , , at , , filament beam
Notice that the on-axis flux reaches a maximum
Photon energy (keV)
Angular flux (ph/s/0.1%bw/mrad2)
This is a tuning curve, here for the angular flux

## Slide 53: Undulator key parameters
Radiated power
The total power radiated from an insertion device is
For an in-vacumm undulator at the ESRF:
,
,

## Slide 54: Undulator key parameters
Photon beam size
where is the electron beam size and is the photon beam size for an filament beam
Photon beam divergence
where is the electron beam divergence and is the photon beam divergence for a filament beam
For Gaussian photon beams
where undulator length.
Electron beam parameters
are the emittance
The define the beam enveloppe

## Slide 55: Undulator key parameters
Brilliance
The brilliance is often* defined as
High brilliance means high flux for a small and collimated photon beam.
A high brilliance is needed for coherence experiments.
*Other definitions of brilliance exists
Photon flux per unit bandwidth
Source size and divergence

## Slide 56
Technology

## Slide 57: Periodic magnetic fields
Permanent magnets
Typically 4 magnets per period. This layout is called a Halbach array
Main limitations
The peak field is limited by the minimum gap
At a given gap, short period undulators produce lower field
(This is true whatever the undulator technology.)
The field is tuned with the gap . It varies as
In some cases, adding iron poles increase the performances

## Slide 58: Undulator technology
Standard permanent magnet undulators
Vacuum chamber
Design view of an undulator
Permanent magnet assembly

## Slide 59: Undulator technology
In-vacuum permanent magnet undulators
Vacuum chamber
Minimum gap reduced by a factor of two compared to standard undulators
Design view of an in-vacuum undulator

## Slide 60: Undulator technology
Cryogenic permanent magnet undulators
Stronger field
Better resistance to demagnetization
Magnetization
Coercitive field
Cooling down
Design view of an in-vacuum undulator

## Slide 61: Electromagnetic insertion devices
Normal conductors cannot compete with permanent magnets at short periods
Superconducting devices
Much higher current densities are reached
Used for high field wigglers
SC undulators developped by some institutes since the early 2000
Low temperature superconducting undulators (LTS) have similar performances as cryogenic permanent magnet undulators
High temperature superconductors (HTS) can change the game if used at low temperature
Developments in progress!

## Slide 62: References
References in the presentation
[Feynman, 1963] R.Feynman et al., The Feynman lectures on physics, Volume 1, Chapter 34, 1963
[Walker, 2003] R. Walker, Bending magnet and wiggler radiation, in Undulators, wigglers and their applications, Ed. H. Onuki and P. Elleaume, Taylor and Francis, 2003
[Walker, 1998] R. Walker, Insertion Devices: undulators and wigglers, in Proc. CERN Accelerator School on Synchrotron Radiation and Free Electron Laser, 1998
[Elleaume, 2003] P. Elleaume, Undulator radiation, in Undulators, wigglers and their applications, Ed. H. Onuki and P. Elleaume, Taylor and Francis, 2003
Others
J. A. Clarke, The science and technology of undulators and wigglers, Oxford University Press, 2004
A. Hofmann, Characteristics of synchrotron radiation, in Proc. CERN Accelerator School on Synchrotron Radiation and Free Electron Laser, 1998

## Slide 63
Thank you!