## Slide 1: The TALYS nuclear model code I
Arjan Koning
Nuclear Data Section, NAPC
International Atomic Energy Agency, Vienna
ICTP-IAEA Workshop on the Evaluation of Nuclear Reaction Data for Applications, Trieste, Italy, October 2-13 2017

## Slide 2: Acknowledgements
Stephane Hilaire and Eric Bauge, CEA-DAM Bruyeres-le-Chatel, France,
Stephane Goriely, Univ. Libre Brussels, Belgium,
Dimitri Rochman, NRG Petten, the Netherlands,
Jura Kopecky, JUKO Research, Alkmaar, the Netherlands,
Stephan Pomp, Univ. Uppsala, Sweden,
for lecture material and useful discussions.

## Slide 3
First, an advertisement……

## Slide 4: Isotope Browser – App for smart phones
Interactive App for Tablet or phone
Provides nuclide properties for 4,000 nuclides and isomers (data from ENSDF)
Android , Apple and Amazon Kindle
~49,000 downloads so far (~1,200 x month)
2 new releases per year
  https://play.google.com/store/apps
  https://itunes.apple.com
Now available in 10 languages:
  English, Arabic, Chinese, French*, Spanish, Russian (6 UN languages), Japanese, Italian, Slovenian, traditional Chinese
*French about to be deployed

## Slide 5: Outline
Nuclear data
General overview of TALYS
A glimpse of some important nuclear models:
  Optical model
  Level densities
  Compound nucleus reactions
  Pre-equilibrium reactions
  Gamma-ray strength functions
  Fission
Installing and running the code

## Slide 6: Nuclear data for applications
All effects of an interaction of a particle (usually: neutron) with a nucleus in numerical form:
Cross sections (total, elastic, inelastic, (n,2n), fission, etc.)
Angular distributions (elastic, inelastic, etc.)
Emission energy spectra
Gamma-ray production
Fission yields, number of prompt/delayed neutrons
Radioactive decay data
Etc.
Complete nuclear data libraries can be obtained through a combination of experimental and theoretical (computational) nuclear physics

## Slide 7: Introduction
Nuclear data is crucial for reactor and fuel cycle analysis:
  Energy production, radiation damage, radioactivity, etc.
  Currently large emphasis on uncertainties: nuclear data uncertainites lead to uncertainties in key performance parameters
More complete and accurate nuclear data for advanced reactor systems does not prove the principle, but
  Accelerates development with minimum of safety-justifying steps
  improves the economy whilst maintaining safety
The nuclear industry claims that improved nuclear data, and associated uncertainty assessment, still has economical benefits of hundreds of million per year

## Slide 8: Nuclear data needs and tools
A well-balanced effort is required for:
High accuracy differential measurements (Europe: IRMM Geel + CERN-nTOF + others)
Nuclear model development and software (e.g. TALYS)
Data evaluation, uncertainty assessment and library production and processing (Europe: JEFF, TENDL)
Validation with simple (criticality, shielding) and complex (entire reactors) integral experiments
All this is needed for both fission and fusion: the approach is similar, the energy range is different.

## Slide 9: Nuclear data cycle
Or TENDL!!

## Slide 10: EXFOR database (Nuclear Reaction Data Center Network: IAEA, NEA, NNDC, JAEA, Obninsk, etc)
Chart: 
| (n,tot) | (n,el) | (n,non) | (n,n') | (n,2n) | (n,g) | (n,p) | (n,a) | (n,f)
Cross section measurements in EXFOR | 4493 | 1118 | 425 | 1838 | 2866 | 5699 | 2561 | 1400 | 1259
Total estimated cost of EXFOR (AK, private comm.): between 20 – 60 Billion Euro
Total estimated value of EXFOR : priceless

## Slide 11
Cross sections :
total, reaction, elastic (shape & compound), non-elastic, inelastic (discrete levels & total)
total particle (residual) production
all exclusive reactions (n,nd2a)
all exclusive isomer production
all exclusive discrete and continuum g-ray production
Spectra :
elastic and inelastic angular distribution or energy spectra
all exclusive double-differential spectra
total particle production spectra
compound and pre-equilibrium spectra per reaction stage.
Fission observables :
cross sections (total, per chance)
fission fragment mass and isotopic yields
fission neutrons (multiplicities, spectra)
Miscellaneous :
recoil cross sections and ddx
particle multiplicities
astrophysical reaction rates
covariance information
TYPES OF NUCLEAR REACTION DATA NEEDED

## Slide 12
PLATYPUS

## Slide 13: GENERAL FEATURES Situation in 1998 !
ALICE – LLNL – 1974 – Blann
(Mc-)GNASH – LANL – 1977 – Young, Arthur & Chadwick
TNG – ORNL – 1980 – Fu
STAPRE – Univ. Vienna – 1980 – Uhl
UNF,MEND – CIAE, Nanking Univ. – 1985 – Cai, Zhang
TALYS – NRG/CEA – 1998 – Koning, Hilaire & Duijvestijn
Modern computers (i.e. speed and memory)
available when the code conception was started
EXIFON – Univ. Dresden – 1989 – Kalka
EMPIRE – ENEA/IAEA/BNL – 1980 – Herman

## Slide 14: GENERAL FEATURES GNASH Input file before 1998

## Slide 15: GENERAL FEATURES Ideas behind TALYS conception
- TALYS mantra : “ First Completeness then Quality”
- Transparent programming
No NaNs
No Crash
Warnings to identify malfunctions
Default « simple » models which will later be improved (anticipation)
All output channels smoothly described
No unnecessary assumptions
No equation simplification (one can recognize a general expression)
Many comments
No implicit definition of variables
The variables are defined following the order of appearance in subroutines

## Slide 16: GENERAL FEATURES What TALYS does !
- Simulates a nuclear reaction
projectiles : n,p,d,t,3he, 4he and gamma
targets : 3 ≤ Z ≤ 124 or 5 ≤ A ≤ 339 (either isotopic or natural)
- Incident projectile energy from a few keV up to 200 MeV
(code “works” up to1 GeV)
- TALYS can be used :
. In depth single reaction analysis
. Global nuclear reaction network calculation (eg astrophysics)
. Within a more global code system (reactor physics)
. Without reaction calculation (only structure data provided)
TALYS is always under development, while a stable version is released
every 2 years.

## Slide 17: GENERAL FEATURES Technical details
- Fortran 77 , gradually evolving into full Fortran95
-  110000 lines (+ 20000 lines of ECIS)
- Modern programming
- Flexible use and extensive validation
- Flexibility : default  4 line idiot proof input (element, mass, projectile, energy)
adjustment  400 keywords
- >500 pages manual
- Drip-line to drip-line calculations help removing bugs
- Random input generation to check stability
- Compiled and tested with several compilers and OS
- modular (312 subroutines)
- Transparent programming (few exceptions)
- Explicit variable names and many comments (30% of total number of lines)

## Slide 18: GENERAL FEATURES Typical calculation times
Numbers based on a single Intel Xeon X5472 3.0 GhZ processor
Time needed to get all cross sections, level densities, spectra, angular distributions. gamma production etc.:
  14 MeV neutron on non-deformed target: 3 sec.
  60 incident energies between 0 and 20 MeV:1 min. (Al-27)
        4 min. (Pb-208)
        10 min. (U-238)
  100 incident energies between 0 and 200 MeV:20 min. (Al-27)
        3-100 hours (U-238) depending on OMP
  60 incident energies between 0 and 20 MeV for all 2808 nuclides, stable or with t> 1 sec: about 200 hours
  To obtain credible Monte Carlo based covariance data: multiply the above numbers by 50-500.

## Slide 19: GENERAL FEATURES TALYS versions online
http://www.talys.eu

## Slide 20: GENERAL FEATURES TALYS users and publications
User feedback via talys mailing list : info@talys.eu to be added to mailing list
: talys-l@nrg.eu to inform mailing list
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
publications | 8 | 7 | 23 | 27 | 33 | 58 | 66 | 75 | 161 | 131
PUBLICATIONS

## Slide 21: GENERAL FEATURES TALYS versions online
http://www.talys.eu
TALYS 1.0 (ND 2007)
TALYS 1.2 (End of 2009)
- new keywords (mainly to improve fitting possibilities)
- bugs corrected to solve crashes or unphysical results
- inclusion of microscopic ph level densities
- inclusion of Skm-HFB structure information (def., masses, g strengths)
- inclusion of D1M
TALYS 1.4 (End of 2011)
- new alpha and deuteron OMP
- URR extension
TALYS 1.6 (End of 2013)
- non-equidistant excitation energy binning possible (extension to energies > 200 MeV)
- direct and semi-direct capture added
- new microscopic lds from D1M
- medical isotope production implemented
- coupling to GEF for fission yields done
TALYS 1.8 (End of 2015)
    Resolved resonance range added
    More extensive GEF and fission possibilities (PFNS) added

## Slide 22: GENERAL FEATURES TALYS Scheme

## Slide 23: TALYS code scheme

## Slide 24
REACTION MODELS & REACTION CHANNELS
(REMINDER)
Optical model
+
Statistical model
+
Pre-equilibrium model
sR = sd + s PE + sCN
n + 238U
Neutron energy (MeV)
Cross section (barn)
= snn’ + snf + sng + ...

## Slide 25
TIME SCALES AND ASSOCIATED MODELS (1/4)
Typical spectrum shape
Always evaporation peak
Discrete peaks at forward angles
Flat intermediate region

## Slide 26
Reaction time
Emission energy
d2s / dWdE
Compound
Nucleus
Pre-equilibrium
Direct
components
TIME SCALES AND ASSOCIATED MODELS (2/4)
MSC
MSD
Low emission energy
Reaction time  10-18 s
Isotropic angular distribution
High emission energy
Reaction time  10-22 s
Anisotropic angular distribution
- forward peaked
- oscillatory behavior
 spin and parity of
residual nucleus
Intermediate emission energy
Intermediate reaction time
Anisotropic angular distribution smoothly
increasing to forward peaked shape
with outgoing energy

## Slide 27
TIME SCALES AND ASSOCIATED MODELS (3/4)
Elastic
Fission
(n,n’), (n,),
(n,), etc…
Inelastic
Tlj
Reaction
Direct (shape) elastic
Direct components
NC
PRE-EQUILIBRIUM
COMPOUND
NUCLEUS
OPTICAL
MODEL

## Slide 28
TIME SCALES AND ASSOCIATED MODELS (4/4)

## Slide 29: GENERAL FEATURES What TALYS yields
Cross sections :
total, reaction, elastic (shape & compound), non-elastic, inelastic (discrete levels & total)
total particle production
all exclusive reactions (n,nd2a)
all exclusive isomer production
all exclusive discrete and continuum g-ray production
Spectra :
elastic and inelastic angular distribution or energy spectra
all exclusive double-differential spectra
total particle production spectra
compound and pre-equilibrium spectra per reaction stage.
Fission observables :
cross section (total, per chance)
fission fragment mass and isotopic yields
Miscellaneous :
recoil cross sections and ddx
particle multiplicities
s and p wave functions and potential scattering radius r’
nuclear structure only (levels, Q, ld tables, …)
specific pre-equilibrium output (ph lds, decay widths …)
astrophysical reaction rates

## Slide 30
Microscopic / Phenomenologic
TALYS simulation by CEA - DAM

## Slide 31
Microscopic / Phenomenologic
Simulation by CEA-DAM

## Slide 32: GENERAL FEATURES TALYS validation
- Validation with the drip code
Drip (not released) performs drip line to drip line calculation
 No Crash
 Checking results smoothness
- Validation with the monkey code
Monkey (not released) creates random input for TALYS
 No Crash
 Checking robustness with respect
to crazy input (within allowed ranges) values
- Statistical analysis of cross sections - SACS (J. Kopecky)
Extensive comparison of cross section with data from EXFOR
 C/E values
 Shape analysis (maximum xs, energy of maximum, half width at maximum)
- Validation of level density models with the kh05 code
kh05 (not released) automatically adjust level densities to data
 global and local level density models
TALYS has then be used to perform extensive comparisons between theoretical and experimental
cross sections for (n,g), (n,2n), (n,p), (n,d) and (n,a) with all possible ld models

## Slide 33: Statistical Analysis of Cross Sections (SACS) by J. Kopecky: (n,p)
Trend line
Discrepant reactions
S=(N-Z)/A

## Slide 34: Nuclear models
Only few slides per model.
See Stephane Hilaire and Stephane Goriely for more details

## Slide 35: Optical model

## Slide 36
THE OPTICAL MODEL
U
Direct interaction of a projectile with a target nucleus considered as a whole
Quantum model  Schrödinger equation
U = V + iW
Complex potential:
Refraction
Absorption

## Slide 37: Neutron total cross sections
A.J. Koning and J.P. Delaroche, KD03 OMP, Nucl. Phys. A713 (2003) 231

## Slide 38: Neutron elastic scattering angular distributions
A.J. Koning and J.P. Delaroche, KD03 OMP, Nucl. Phys. A713 (2003)

## Slide 39
Level density
?

## Slide 40: Level density definition

## Slide 41: Fermi gas level density

## Slide 42
THE LEVEL DENSITIES
(Qualitative aspects 1/2)
Exponential increase of the cumulated number of discrete levels N(E) with energy
   rho(E)=
   odd-even effects
Mean spacings of s-wave neutron resonances at Bn of the order of few eV
   rho(Bn) of the order of 104 – 106 levels / MeV
56Mn
57Fe
58Fe
E (MeV)
N(E)
dN(E)
dE
increases exponentially
Incident neutron energy (eV)
Total cross section (b)
n+232Th

## Slide 44
THE COMPOUND NUCLEUS MODEL
(basic formalism)
Compound nucleus hypothesis
Continuum of excited levels
Independence between incoming channel a and outgoing channel b
ab
=
(CN) Pb
a
(CN) = Ta
a
p
ka
2
Pb=
Tb
S Tc
c
 Hauser- Feshbach formula
=
ab
p
ka
2
Ta Tb
S Tc
c

## Slide 45
THE COMPOUND NUCLEUS MODEL
(qualitative feature)
Compound angular distribution & direct angular distributions
45° 90° 135°

## Slide 46
THE COMPOUND NUCLEUS MODEL
(multiple emission)
E
N
Nc-1
Nc
Nc-2
Z
Zc
Zc-1
Sn
Sp
Sa
Sn
Sp
Sa
n’
n’
n(2)
fission
Sn
Sa
Sn
Sp
Sa
p
Jp
Sn
Sp
Sa
a
Sn
Sp
Sa
d
g
g
g
n
n
Target
Compound Nucleus
+ Loop over CN spins and parities

## Slide 47
THE PRE-EQUILIBRIUM MODEL
(Exciton model principle)
Compound
Nucleus
EF
0
E
time
1p
1n
2p-1h
3n
3p-2h
5n
4p-3h
7n

## Slide 48
THE PRE-EQUILIBRIUM MODEL
without pre-equilibrium
Incident neutron energy (MeV)
Outgoing neutron energy (MeV)
Compound nucleus
d/dE(b/MeV)
(barn)
14 MeV neutron + 93 Nb
without pre-equilibrium
pre-equilibrium

## Slide 49: Conclusions
TALYS is the most versatile (subjective) and most used (objective) model code in the world for nuclear reactions up to 200 MeV.
Exciting new nuclear structure developments can go straight into the code.
The road to technology (nuclear data libraries) and applied science (astrophysics) is entirely automated.

## Slide 50: Thank you!
Notes: Thank you!