## Slide 1: TALYS exercises II
Arjan Koning
Nuclear Data Section, NAPC
International Atomic Energy Agency, Vienna
ICTP-IAEA Workshop on the Evaluation of Nuclear Reaction Data for Applications, Trieste, Italy, October 2-13 2017

## Slide 2: Exercises
Continue exercises of yesterday
Or
Try the 3 new exercises given below
Or
Ask us about cases you are interested in

## Slide 3: TALYS sample cases (see manual)
232Th

## Slide 4: TALYS sample cases (see manual)

## Slide 5: TALYS sample cases (see manual)

## Slide 6: TALYS sample cases (see manual)
19. Unresolved resonance range parameters: n + 136Ba
20. Maxwellian averaged cross section at 30 keV: n + 138Ba
21. Medical isotope production with p + 100Mo
22. Calculations up to 500 MeV for p + 209Bi
23. Neutron multiplicities and fission yields for n + 242Pu
24. Local parameter adjustment for n + 93Nb
25. Direct neutron capture for n + 89Y

## Slide 7: Exercise: Subactinide fission
Projectile n
Element Bi
Mass 209
Energy 30. 80. 10.
Fission y
xmgrace fission.tot

## Slide 8: Exercise 5 of TALYS manual

## Slide 9: Exercise: n + 232Th
Samples/5/new/
Take only a few low energies!! (edit energies and
throw away most of the file)
Change fission barrier of Th233 and see
what happens
xmgrace –settype ../plot/fission.exp
–settype xy fission.tot
Next run: Add
Fymodel 2
Massdis y
To get the fission yields (GEF model)

## Slide 10
Etc. etc.

## Slide 11: TALYS-1.8 reconstructs resonances (Thanks to Red Cullen and PREPRO codes)

## Slide 12: Reactions with resonances
TALYS can read in resonance parameters and reproduce the pointwise cross sections.
Run samples/27/a/new
n + Y89
Smooth “TALYS-only” capture cross section: rp039090.tot
File with resonances: xs000000.tot
xmgrace rp039090.tot xs000000.tot
Run samples/27/b/new
Add the xs000000.tot file from this directory to the previous plot command to show all 3 curves.

## Slide 13: Thank you!
Notes: Thank you!