## Slide 1: Introduction to energy sector representation in the template CLEW model

## Slide 2: Template model energy system
  Standardized model structure
    Customizable to country data
    Structure customizable for country projects
  Focus on power sector
    More technology detail
  Simplified demand representation
    Fuel projections based on selected drivers
  Simplified primary energy supply representation
    Single source representation

## Slide 3: Energy sector model structure
Fossil fuels
Domestic extraction
Renewable resources
Energy
imports
Fuels
Renewable fuels
Energy exports
Power sector
Oil
Refinery
Fuels
Primary Energy Supply
Energy Transformation
Biofuel production
Agricultural sector
Commercial sector
Industrial sector
Residential sector
Transport sector
Final energy demand
Refined products
Renewable fuels
Electricity
Fuel demand
Fuel demand
Fuel demand
Fuel demand
Fuel demand

## Slide 4: List of sectors, commodities and abbreviations
Sector name | Sector abbreviation | Commodity name | Commodity abbreviation | Commodity name | Commodity abbreviation
Agriculture | AGR | Biomass | BIO | Kerosene | KER
Commerce | COM | Charcoal | CHC | Liquid petroleum gas | LPG
Industry | IND | Coal | COA | Natural gas | NGS
Power | PWR | Crude oil | CRU | Other hydro carbons | OHC
Residential | RES | Diesel | DSL | Petroleum coke | PCK
Transformation | UPS | Geothermal | GEO | Solar energy | SOL
Transport | TRA | Gasoline | GSL | Uranium | URN
 |  | Heat | HET | Waste | WAS
 |  | Fuel Oil | HFO | Wind energy | WND
 |  | Hydro | HYD |  | 
Notable exception: Electricity before transmission (ELC001) and after transmission (ELC002)

## Slide 5: Naming conventions
  Commodity naming convention in Osemosys model:
    At “wholesale” level 3 letter code as per table on previous slide
    At sector level: 3 letter sector abbreviation + 3 letter commodity abbreviation
    Examples:
      Diesel (DSL) used in agriculture (AGR) = AGR+DSL=“AGRDSL”
      Natural gas (NGS) used in industry (IND) = IND+NGS=“INDNGS”
      Coal (COA) used in industry (IND) = IND+COA=“INDCOA”
      Gasoline (GSL) used in transportation (TRA) = TRA+ GSL=“TRAGSL”
      Wind energy (WND) used in power generation (PWR) = PWR+ WND=“PWRWND”

## Slide 6: Demand side
  No technology representation on demand side
    Projected fuel demand in 5 economic sectors
    Agriculture (AGR), Commerce (COM), Industry (IND), Residential (RES), Transport (TRA)
    Endogenous demand for some fuels
  Excel energy demand template available for data management, simple projections
    Includes MoManI import tables.

## Slide 7: Power sector
  11 technology fuel groups (e.g. coal, hydro, natural gas, wind)
    2-6 technologies per group
  Naming:
    “PWR” + 3 letter fuel abbreviation + 3 digit Number
    E.g. Wind power plant #3: PWRWND003
    Hydro power plant #6: PWRHYD006
    Diesel power plant #1: PWRDSL001
  Power sector excel template available for data entry and management
    Includes MoManI import tables.

## Slide 8: Transformation sector
  Oil refinery
    Converts crude oil to refined products
    Technology: UPSCRU001
  Charcoal production
    Converts biomass to charcoal
    Technology: UPSBIO001
  Biofuel production
    Converts a crop (from the land-use model component) to biofuels
    Technology: UPSBIO002

## Slide 9: Additional notes on technologies and naming
  Distribution technologies for sectoral demand
    Allows for accounting of sectoral demand, sector specific distribution costs and energy requirements for distribution
    Naming convention: “DEM” + 3 letter sector abbreviation + 3 commodity abbreviation
    Example: Natural gas distributed to the commercial sector: DEMCOMNGS
  Mining/Extraction technologies
    Naming: “MIN” + 3 commodity abbreviation, e.g. MINCOA (Coal mining)
  Renewable resource technologies
    Naming: “RNW” + 3 commodity abbreviation, e.g. RNWSOL (Solar energy resource)
  Import technologies
    Naming: “IMP” + 3 commodity abbreviation, e.g. IMPCRU (Crude oil imports)
  Export technologies
    Naming: “EXP” + 3 commodity abbreviation, e.g. EXPNGS (Natural gas exports)