## Slide 1: Ultrashort Pulse Shaping
Giorgia Sparapassi
Winter College on Extreme Non-linear Optics, Attosecond Science and High-field Physics
06/02/2018 - ICTP (Trieste)
Notes: Good afternoon, my name is Giorgia and I am a PhD student here in Trieste, working in an ultrafast spectroscopy laboratory at Elettra.
Let me start by thanking the organizers of the college for the opportunity they gave to be here on this side today, to discuss with you a technique I am getting familiar with which is Pulse Shaping.
In these first two days of this college we have had the chance of learning about the history of laser physics. We know that they can generate ultrashort pulses with a duration on the picosecond, femtosecond and attosecond time scale. We also learned that there are many ways in which you can characterize these pulses. Today I will introduce you to a field which is developing side by side with these other techniques, ultrashort p.s. This is quite a broad field at the moment due to the fact that several technologies are under perfectioning, I will introduce you to the most popular approaches to Pulse Shaping.

## Slide 2: Goals of pulse-shaping
Shape the temporal and spectral profile of the pulse for
  Pulse compression/stretching
  Envelope phase/delay control
  Replica generation
  Spectral filtering
  Information encoding/decoding
  …
Laser
Pulse shaper
Notes: The application space for ultrashort pulses has become extremely broad, including laser-matter interactions, ultrafast time-resolved spectroscopy, metrology, processing of materials, nonlinear microscopy, optical communications, and radiofrequency signal processing.
Pulse shaping and processing technologies are complementary to ultrashort pulse generation and characterization methods and are now widely applied.

## Slide 3: Pulse shaping by linear filtering
x(t)
t
y(t) = (x∗ h) (t) = ∫ x(t’) h(t-t’) dt’
Y(w) = X(w) H(w)
Impulse h(t)
?
Frequency H(w)
X(w)
x(t)
t
Response functions
Y(w)
Very hard to act on the pulse on the femtosecond time scale & very convenient to use frequency dispersion

## Slide 4: Zero dispersion line or 4f-line
“4f line”
f
f
f
f
X(w)
Y(w)
x
A pair of identical dispersive elements and lenses
Fourier plane
Notes: What I show here is a basic setup for Fourier transform optical pulse shaping, a widely adopted approach.
Each spectral component is angularly dispersed by the first grating then focused close to small diffraction spots in the Fourier plane by the first lens/mirror. Thus, in this plane, all the spectral components are spatially separated and focused. Then a second combination of lens/grating allows recombining all the frequencies into a single collimated beam. If nothing is placed in the Fourier plane then the device is dispersion free (zero dispersion line) and the output beam is identical to the input one.

## Slide 5: Mask at the Fourier plane of a 4f-line
Convenient to exploit spatial dispersion by using a spatial “mask” M(x) at the Fourier plane
Focal spot size of a spectral component: X0 =
Linear dispersion: =
Eout(w,x) = Ein(w,x) M(x)
Ein(w,x) = X(w) e
The mask is designed with the purpose of obtaining the desired Y(w)
Y(w)
Fourier plane
X(w)
d
x
X0
Ein(w,x)
Eout(w,x)
M(x)

## Slide 6: Amplitude and phase masks
Fourier plane
Two masks can be used, one modulating the amplitude of the spectral components,
one modulating the phase of the spectral components
X(w)
Y(w)
x
M(x) = |M(x)| ei fM(x)

## Slide 7: Mask: Gaussian approximation
Y(w) = H(w)X(w)
Selecting the fundamental Hermite-Gaussian mode
H(w) = M(x’) e dx’
x
X(w)
M(x)
Ein(w,x)
Eout(w,x)
Spatially filtering the beam after the FP
Convenient to exploit spatial dispersion by using a spatial “mask” M(x) at the Fourier plane
Fourier plane
Notes: To obtain this expression, we have implicitly assumed that the spatial profile is unaffected by the mask, which is a strong simplification. As a consequence, this expression is only valid for sufficiently smooth and simple shapes.

## Slide 8
M(x)
Square waveform
Noise bursts
Pulse train
M(x)
M(x)
Time delay [ps]
Time delay [ps]
Intensity [a.u.]
Intensity [a.u.]
Cubic, flat,
quadratic
phase gradient
Time delay [ps]
Time delay [ps]
-4 -3 -2 -1 0 1 2 3 4
-4 -3 -2 -1 0 1 2 3 4
Intensity [a.u.]
Intensity [a.u.]
Mask examples
*phase only
*phase only
*phase only
*amplitude only
Multiple masks allow independent amplitude and phase modulation but cannot be modified during experiment

## Slide 9: 4f-line pulse-shapers
  Static mask (SM) are a special case of this approach!
  Micro-machined deformable mirror (mDM)
  Acousto-optic modulator (AOM)
  Spatial light modulator (SLM)
Programmable
PC
Notes: The programmability feature of pulse shaping is very important, allowing a single apparatus to generate a wide range of waveforms for different experiments or applications.

## Slide 10: 4f-line pulse-shapers
  Micro-machined deformable mirror (mDM)
Actuator electrodes
Printed circuit board for applying electrostatic potential DV with a software controlled pattern
Deformable membrane (Si3N4) with reflective coating (material depends on wavelength)
Anchoring posts
DV
Optics Letters, 1999, 24.7: 493
Notes: Thie uDM is commonly used for correction of non-linear effects. It is composed of a coated membrane suspended over an array of actuator electrodes on a printed circuit board. The deformation of the reflecting surface is governed by electrostatic force. Such a mask is placed in the Fourier plane of a folded 4f-line.
It allows smoothly varying phase only modulation, in addition to low losses and relatively high actuator density. It represents a fairly low cost solution which could be extended on a very broad spectral range depending on the coating of the mirror.

## Slide 11: 4f-line pulse-shapers
  Micro-machined deformable mirror (mDM)
  www.okotech.com
Actuator electrodes
Interferometric testing of a mDM for:
No voltage applied
Voltage applied on all electrodes
Voltage applied on 20-37 electrodes
Voltage applied on randomly chosen electrodes
a)
b)
c)
d)

## Slide 12: 4f-line pulse-shapers
  Micro-machined deformable mirror (mDM)
The membrane deforms according to the applied voltage (DV)2
Phase only modulation
introducing a continuous optical path difference:
df (l,DV)
Allows to build high order phase gradients
Path difference allows phase modulation
Notes: Thie uDM is commonly used for correction of non-linear effects. It is composed of a coated membrane suspended over an array of actuator electrodes on a printed circuit board. The deformation of the reflecting surface is governed by electrostatic force. Such a mask is placed in the Fourier plane of a folded 4f-line.
It allows smoothly varying phase only modulation, in addition to low losses and relatively high actuator density. It represents a fairly low cost solution which could be extended on a very broad spectral range depending on the coating of the mirror.

## Slide 13: 4f-line pulse-shapers
Acousto-Optic crystal (TeO2, Ge, fused Si)
Piezoelectric transducer
Software- controlled modulating RF voltage delivering an arbitrary waveform (beware of acoustic attenuation and nonlinearities)!
Period = vAC/fRF
∿
  Acousto-optic modulator (AOM)
Acoustic wave f(x=t/vAC)
Refractive index variation induced by the traveling acoustic wave
Finite travel time of AW
(can be reprogrammed every ~ms)
AW has limited lifetime
Notes: Acousto-optic (AO) modulators have also been used for programmable Fourier transform pulse shaping. The spatial mask pattern is driven by a temporal radiofrequency voltage signal, converted into a traveling acoustic wave by a piezoelectric transducer. Scaled into space by the acoustic velocity (Vac) in the AOM crystal, it acts as a refractive index grating.

## Slide 14: 4f-line pulse-shapers
Phase difference between 1st and 0th order
f(l,fRF) =
∿
  Acousto-optic modulator (AOM)
Induced diffraction grating allows amplitude and phase modulation
1st order max for sin() =
(phase matching condition)
From 260 nm to 5 μm
UNDIFFRACTED LIGHT
Tilting of FP
Notes: The spatial mask pattern is driven by a temporal radiofrequency voltage signal, converted into a traveling acoustic wave by a piezoelectric transducer. Scaled into space by the acoustic velocity (Vac) in the AOM crystal, it acts as a refractive index grating.
The diffracted beam is shifted in frequency by an amount equal to the electrical drive frequency (typically in the one hundred MHz range), ideally with an amplitude and phase that directly reflect the amplitude and phase of the RF drive.

## Slide 15: 4f-line pulse-shapers
  Liquid crystal based spatial light modulator (LC SLM)
Liquid crystals (nematic phase)
Transparent ITO film
DV
= 0
≠ 0
(birefringence reduced)
x
x
z
x
z
z
y
Each pixel is a waveplate introducing an angle f(w,DV) = t
IR to UV
Glass
Transparent pixelated indium tin oxide (ITO) film
Glass
anchorage direction
anchorage direction
Notes: Each pixel of a liquid crystal spatial light modulator (LC-SLM) is a programmable waveplate controlled by voltage. An LC-SLM consists of a thin layer of nematic liquid crystal placed between two glass substrates. One substrate is covered with transparent ITO (indium tin oxide) electrodes which allow the application of independent voltages to each pixel. The nematic liquid crystals are small rods which are oriented parallel to the substrate when no voltage is applied. When a voltage is applied, the nematic molecules tend to align along the field. This modifies the birefringence of the medium, leading to a modification of the optical path for light polarized along the anchorage direction.

## Slide 16: 4f-line pulse-shapers
  Liquid crystal based spatial light modulator (LC SLM)
  Single-layer 1D arrangement
The optical path-length difference is adjustable for each wavelength and enables spectral phase modulation
The incoming light is polarized along the anchorage axis
+90°

## Slide 17: 4f-line pulse-shapers
  Liquid crystal based spatial light modulator (LC SLM)
  Double-layer 1D arrangement
Phase and amplitude shaping with complex transfer function
H(w) =
Pol. axis:
90°
Pol. axis:
90°
Anchorage directions:
+45° & -45°

## Slide 18: 4f-line pulse-shapers
  Liquid crystal on silicon based spatial light modulator (LCoS SLM)
  Single-layer 2D arrangement
DV
x
z
y
Silicon layer with pixelated electrodes
anchorage direction
Reflective layer
LCos SLM
Folded geometry
Incoming & outgoing beams
Very high electrode density

## Slide 19: 4f-line pulse-shapers
  Liquid crystal on silicon based spatial light modulator (LCoS SLM)
  Single-layer 2D arrangement: effects of pixelization
Gaps are usually ~ mm wide
Portion of incident pulse reflected by gaps (not shaped)
Linearly chirped pulse (shaped)
Pixel size: tens of mm

## Slide 20: In-line pulse-shapers
∿
Acousto-optic programmable dispersive filter (AOPDF)
Ordinary axis
Extraordinary axis
Acousto-Optic crystal
Acoustic wave
x
RF waveform generator and acoustic transducer
Incoming collimated beam
www.fastlite.com
Notes: An alternative system, appeared in the 90’s was called AOPDF or Dazzler (in its commercial name).
An acoustic waveform is launched along a crystallographic plane. This is controlled by connecting a radio-frequency arbitrary waveform generator to the acoustic transducer, thus programmability is easily achieved.
An acoustic wave propagates with a velocity V along the z axis and produces a periodic, stress-induced birefringence that couples light from the input polarization into the orthogonal polarization state (which is transmitted by the polarizer).

## Slide 21: In-line pulse-shapers
Acousto-optic programmable dispersive filter (AOPDF)
Ordinary axis
Extraordinary axis
x
Diffraction allows amplitude and phase modulation
Incoming light is polarized along the ordinary axis
EOUT(w) EIN(w) SAC (bw)
b = Dn (vAC/c)
Acoustic wave – light wave coupling: diffraction on the orthogonal polarization occurs when x-dependent phase matching conditions are fulfilled:
Amplitude of diffracted spectral components depends on acoustic wave strength
wE = wAC(x) + wO
E(wE) = AC(wAC(x)) + O(wO)
Nonlinear effects (high peak intensity)
Refresh rate limited by AW propagation (~ps)
Notes: It is based on the acousto-optic interaction between a controlled acoustic wave f(t) and an optical ultrashort pulses E(t).
Every frequency v travels a certain distance before it encounters a phase-matched spatial frequency in the acoustic grating. At this position z, part of the energy is diffracted into mode 2. The pulse leaving the device at mode 2 will be made of all the spectral components that have been diffracted at various positions and hence reproduces spatially the temporal shape of the rf signal.

## Slide 22: Comparison between different pulse shapers
Type | Advantages | Trade-offs
SM | Independent amplitude and phase modulation | Cannot be modified during experiment
mDM | Computer controlled High order spectral phase control Smooth phase variations High actuator density | Phase only modulation
AOM | Computer controlled Can be reprogrammed every ~ms No sharp boundaries | Efficiency limited by imperfect phase matching Distortions introduced by RF waveform amplitude Acoustic wave (AW) has limited lifetime
SLM | Computer controlled High waveform complexity Polarization control | Pixelation & gaps effects Refresh rate limited by LC rotation time (~ms)
AOPDF | Computer controlled Can be reprogrammed every ~ps No sharp boundaries | Nonlinear effects (high peak intensity) Imperfect synchronization of AW to pulses

## Slide 23: Comparison: resolution
Type | Temporal window | Frequency resolution
4f | T 1 / | = /
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
Type | Temporal window | Frequency resolution
4f |  | 
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
Focal spot size of a spectral component
r0
Dispersion between spectral components
M(x)
d
x
r0
f
f
rin
T
2010 J. Phys. B: At. Mol. Opt. Phys. 43 103001
Notes: Now let’s in turn discuss how we could calculate the frequency resolution of a pulse shaper of the 4f type.
The geometry of such a line suggests that the frequency resolution is related to the spacing between the spectral components at the focal plane.
So we calculate the focal spot size of every spectral component and divide it by the angular dispersion given by the grating. This determines dw.
The inverse of dw is called temporal window and is an important parameter to account: it defines a temporal upper bound to the duration or the delay of a shaped pulse. It is like

## Slide 24: Comparison: resolution
The mask acts on more than one spectral component
(finite size focus, finite beam size, mask spatial features too fine).
Can show up also as an amplitude modulation after a phase only mask
Type | Temporal window | Frequency resolution
4f | T 1 / | = /
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
Type | Temporal window | Frequency resolution
4f |  | 
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
2010 J. Phys. B: At. Mol. Opt. Phys. 43 103001
M(x)
d
x
r0
f
f
rin
Spatio-temporal coupling
(T )
Notes: We can also note that the temporal window for a 4f line is related to the input waist r_in. This dependence on geometrical factors is a manifestation of the so called spatio-temporal coupling at the fourier plane.
This can lead to strong spatial distortions in the output waveform.
Let us consider the generation of a train of pulses by applying a phase mask. This is illustrated in the figure where the pulse profile is plotted versus time (horizontal axis) and space (vertical axis) for various programmed delays: as the delay is changed, the pulse appears to move along a slanted line (black dash). Thus the temporal profile of the pulse has an influence on the spatial profile.

## Slide 25: Comparison: resolution
Ordinary axis
Extraordinary axis
Acousto-Optic crystal
Optical wave
x
Input light wave
Type | Temporal window | Frequency resolution
4f | T 1 / | = /
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
Type | Temporal window | Frequency resolution
4f |  | 
AOPDF | T = Dng L cos2(qin) / c | dl = l2 / (cDnLcos2(qin) )
The window and the spectral resolution in an AOPDF are determined mainly by the crystal thickness and its anisotropy
θin is the angle between the incident wave vector and a reference crystallographic axis
L is the length of the AO crystal
Notes: Now let us turn to the AOPDF. Let us start by the temporal window.
T is mainly determined by the crystal thickness and its anisotropy. It is calculated subtracting the time it takes to the optical wave to propagate along the extraordinary axis and the time it takes to the optical wave to travel along the ordinary axis, with a geometrical factor. The frequency resolution is determined by the geometry and the difference between the refraction indexes of the two axes.
We get to a comparison between the best resolutions get so far, with an SLM for the 4f lines and with an AOPDF. They are respectively 0.17 THz

## Slide 26: Case study: our experiment
We want to uncover the statistical correlations introduced in the sample by the material,
thus we need to shape differently each mask and independently in phase and amplitude
BS
Pump
Probe
Probe
Sample
Laser
Spectrometer
D
Pulse shaper

## Slide 27: LCoS SLM-based pulse shaper @ T-ReX
LCoS SLM
Diffraction grating
Cylindrical lens
Incoming & outgoing pulses
(beams are sligthly angled)
Folded 4f line: reflection geometry

## Slide 28: LCoS SLM-based pulse shaper @ T-ReX
Main characteristics of this SLM:
  512 x 512 pixels matrix (total size: 12.8 x 12.8 mm)
  25 mm x 25 mm pixel pitch
  Low inter-pixel cross talk
  Diffraction efficiency 88%
  The beam is dispersed, can be used with high power
  Arbitrary waveform can be chosen

## Slide 29: LCoS SLM-based pulse shaper @ T-ReX
Other elements in the setup:
  Diffraction grating with 1800 g/mm
  qi = 50°, qd = 40°
  Focal length of lens f = 100 mm
LCoS SLM
Diffraction grating
Cylindrical lens
Incoming & outgoing pulses
(beams are sligthly angled)
Folded 4f line: reflection geometry
Laser beam parameters:
  l0 = 375 THz
  Incoming beam radius rin = 2 mm
Spectral features at the FP:
  Focus of a frequency X0 = 29 mm
  Angular dispersion a = 78.5 mm/THz
  Frequency resolution dw = 0.06 THz

## Slide 30: LCoS SLM 2D patterns
Sawtooth with amplitude A(n) and period d
Spectral phase f(n)
2005 Opt. Lett. 30 (3) 343
Build 2D mask starting from amplitude and phase:
A(n)
f(n)
n
n
0 1
0 1
Optimization
0 1

## Slide 31: Shot-to-shot and point-by-point
Phase and amplitude modulation
0 1
Amplitude modulation
0 1

## Slide 32: Conclusions
Several kinds of pulse shapers are available
  Advantages & trade-offs have to be considered
Pulse shapers are very versatile tools, and allow to:
  Optimize the output of a laser
  Produce any waveform from the pulses
  Delay, replicate pulses
  Filter the spectrum
  Change spectral phase
  Add noise on top of the spectrum
  …

## Slide 33: T-ReX group @ Elettra
Daniele Fausti
Group Leader
Alexandre Marciniak
PostDoc
Filippo Glerean
PhD student
Francesca Giusti
PhD student
Jonathan Tollerud
PostDoc

## Slide 34: Thank you for your attention!