## Slide 1
2-year observation of Organic Aerosol properties
In Cape Corsica
J. Sciare, and co-workers @ LSCE

## Slide 2
Cape Corsica monitoring activities
Aerosol Chemistry by ACSM
2012
2013
2014
ACTRIS-ACSM
Intercomparison
exercise at LSCE
ACSM
Intercomparison
exercise at LSCE
Instrument & Stations
failures
+ 535 days (24h) of valid ACSM data
+ A unique dataset to investigate sources (primary/secondary) and geographic origin of OA in W. Mediterranean
+ A component of the ACTRIS-ACSM network (QA/QC controlled datasets)
Comparison with SMPS data
(2012-2014)

## Slide 3
Cape Corsica monitoring activities
Aerosol Chemistry by ACSM
Concentration
µg/m3
Concentration
µg/m3
Concentration
µg/m3
Maximum of OA and SO4 during summertime (max of OA in winter in continental France)
Most the difference between PM1 and PM2.5 relies on primary natural sources (sea salt and dust)

## Slide 4
Seasonal variability of the oxidation state of Organic Aerosols (OA) in Corsica
Temporal variability of specific organic fragments (f44, f43) related to Acid (CO2+) and non-acid (C2H3O+ & C3H7+) OOA
Kroll et al., Carbon oxidation state (OSc) as a metric for describing
the chemistry of atmospheric organic aerosol, Nature, 2011
= oxidation State of OA
1. Highly oxidized OA for 6 months of the year (from April to August)
2. Less oxidized OA for 3 months of the year (from November to January)
2-year ACSM observations

## Slide 5
LV -OOA
Triangle plot from Ng et al. (ACP, 2010)
f43 (non-acid fragment in OOA)
f44 (Acid fragment in OOA)
Min OSc = November
Max OSc = August
Seasonal variability of the oxidation state of Organic Aerosols (OA) in Corsica
SV-OOA
LV –OOA : Low volatile (aged) oxidized OA
SV-OOA : Semi-volatile (fresh) oxidized OA

## Slide 6
Seasonal variation of HOA and OOA
(results from 15-month observations)
OOA
70% of OA during winter months
85% of OA during summer months
On a yearly average
HOA = Hydrogen-Like Organic Aerosol
primary –combustion- aerosols)
OOA = Oxygen-Like Organic Aerosol
(secondary OA)
Seasonal variability of
OA sources in Corsica

## Slide 7
 A factor 10 in the variability of OA concentrations BUT oxidation state of OA (f44, f43) remains very high and poorly variable (few percents)
Oxidation state of in Corsica:
Focus on the Summer 2013 campaign
ADRIMED
SAFMED
f44 (Acid OOA)
f43 (Non-Acid OOA)
Aerosol chemical composition in PM1
determined by the ACSM

## Slide 8
POLTRACK V1.0.2 beta Quick Source mapper
Date: 05/06-05/08/2013 / Hourly mean data / Hysplit – GDAS data
Restricting data to air masses lower than 1000m / Reject backtrajectories: less 2 per 0.1°x0.1° grid cell
Smoothing Kernel-Gaussian function: 5
Scale Nb Occurrence 0 – 5
Occurrence of air masses
Scale [OM] = 0 - 5µg/m3
Organic Aerosol sources
([OA])
Oxidation state of in Corsica:
Focus on the Summer 2013 campaign
Scale OSc 0 – 1
Organic Aerosol oxidation state
(OSc)
 The largest emitting OA region influencing Cape Corsica during summer 2013 are continental originating from Italy and Central/Eastern Europe
 The most oxidized OA are found for marine (highly processed) air masses (e.g. not fed by continental emissions)

## Slide 9
f44 (Acid OOA)
f43 (Non-Acid OOA)
10:00 LT (morning)
21:00 LT (evening)
 Photochemically-induced formation/destruction of non-acid OOA (f43)
 Photochemically-induced formation of acid OOA (f44). Possibly with fragmentation
ACSM – Oxidation State of OA

## Slide 10
Conclusions
From the 2-year observation of PM1 chemical composition with ACSM at Cape Corsica …
Seasonal cycles of OA and SO4 (max in summer) in opposite phase compare to Northern France
Highly oxidized OA in Cape Corsica all over the year (70% during winter to up to 85% of OA in summer)
Seasonal cycle of the oxidation state of OA with minima in November and constant increase
Ambient chemical composition of PM1 a factor of 3 lower from compared to Northern France
During the SAFMED (summer 2013) campaign …
July 2013 characterized by the highest PM1, OA, and SO4 levels observed from mid-2012 till mid-2014 (apart from the pollution episod observed in March 2014)
Stable oxidation state of OA (independent of air masses origin) although [OA] have shown variability of a factor of 10
Diurnal variability in opposite phase for f44 and f43 (e.g. photochemically locally induced formation/destruction of non-acid OOA) concomittant with a decrease in the OM/OC ratio (seen by two different approaches)
Evidence of continental emissions of OA and higher oxidation state above the marine areas